## Slide 1: Click to add title
Click to add subtitle
2nd MEIC Collaboration Meeting October 5-7, 2015
MEIC Program Status
Fulvia Pilat

## Slide 2: Outline
Recall baseline
Program Update since last Collaboration Meeting (March 2105)
Plans for:
Design, R&D, Engineering (FY16-17)
Selected design and R&D topics
At the Collaboration Meeting:
Collect Further input and feedback to plans
Discussion of priorities
Plan and Expectations for the next 6 months (talk)
After the Collaboration Meeting
Establish and communicate priorities for R&D funding
Plan Pre-Conceptual Design Report

## Slide 3: Design Strategy: High Luminosity and polarization
The MEIC design concept for high luminosity is based on high bunch repetition rate CW colliding beams
Beam Design
High repetition rate
Low bunch charge
Short bunch length
Small emittance
IR Design
Small β*
Crab crossing
Damping
Synchrotron radiation
Electron cooling
KEK-B already reached above 2x1034 /cm2/s
All rings are figure-8  critical advantages for both ion and electron beam polarization
  Spin precessions in the left & right parts of the ring are exactly cancelled
  Net spin precession (spin tune) is zero, thus energy independent
  Spin is easily controlled and stabilized by small solenoids or other compact spin rotators

## Slide 4: MEIC Baseline
Baseline for the cost estimate
Collider ring circumference: ~2200 m
Electron collider ring and lines : PEP-II magnets, RF (476 MHz) and vacuum chambers
Ion collider and booster ring: super-ferric magnets
SRF ion linac
Electron cooling: DC cooler and single-pass ERL, bunched-beam e-cooler
Energy range
Electron: 3 to 10 GeV
Proton: 20 to 100 GeV
Lead ions: up to 40 GeV
Design point | p energy (GeV) | e- energy (GeV) | Main luminosity driver
low | 30 | 4 | space charge
medium | 100 | 5 | beam beam
high | 100 | 10 | synchrotron radiation

## Slide 5: Baseline Layout
Ion Source
Booster
Linac
Ion Source
Booster
Linac
MEIC Cost Review December 18 2014
CEBAF is a full energy injector.
Only minor gun modification is needed
Warm Electron
Collider Ring
(3 to 10 GeV)

## Slide 6: Updates from last MEIC CM
Last MEIC CM in March 2015, soon after the January EIC Cost Review
Focus on:
Baseline design optimization
100 MEV SRF linac option
Racetrack vs. figure-8 (Figure-8 for collider, studying racetrack option for booster)
Emittance reduction in the e-ring
Synchronization
ERL Cooler design group started, cooling simulations
Nonlinear Correction design group (SLAC/JLAB)
Polarization: design updates and tracking
Collective effects
Beam formation
R&D,
External review of R&D for super-ferric program
Internal reviews of: SRF R&D including crab cavity and Engineering
MEIC related LDRD proposals  Selected magnetized source R&D, e-cooling modeling, nuclear gluons with charm
Engineering, ESH&Q, Civil
Started engineering support activities (magnets, PEP-II…)
Started soil evaluation study (funding from VA)
Started study of radiation protection

## Slide 7: MEIC Organization
Hugh Montgomery
Bob McKeown
Accelerators
Fulvia Pilat
Physics
Rolf Ent
Design
Yuhong Zhang
Engineering
Tim Michalski
Cost Estimate
Leigh Harwood
R&D
Fulvia Pilat
MEIC Organization established in July 2014
Funding: NP Accelerator R&D, JLAB re-direct, LDRD, SBIR, Commonwealth of Virginia
Facilities
Rebecca Yasky

## Slide 8: MEIC Design Plan
Design activities are mostly based in CASA at JLAB
Redirected resources to MEIC in 2015, effort level constant for FY2015-16
Acknowledge input from Mike Spata (CASA Director) and Yuhong Zhang (MEIC Design Leader)

## Slide 9: MEIC Pre-project R&D plan
The MEIC pre-project R&D level is cost-effective , total <5M$
Resources so far from NP EIC R&D funds, LDRD, SBIR
Anticipate increase of NP EIC R&D funds in FY16 after the LRP recommendation
(Meeting at NP November 12)
Request submitted to VA for 2.4 M$ in FY16-17 for MEIC Accelerator R&D

## Slide 10: MEIC Engineering Plan
We initiated Engineering support work in FY15, and plan to ramp up in FY16-17
Resources mostly internal redirect (12 GeV Project accelerator completed and overall
Project ramping down)
Acknowledge input from Tim Michalski (MEIC Engineering Leader)

## Slide 11: Ion Injector: Short, Lower Energy/Cost Linac
Proton KE: 285  130 MeV
Lead ions: 100  42 MeV
QWR/HWR cryomodules: 16  5
Total lengths: 110  55 m
Total cost: ~factor 3 reduction
Parameter | Units | Value
Ion species |  | H+ to Pb
Fundamental frequency | MHz | 100
KE of H- & lead ions | MeV/u | 130&42
Maximum pulse current Light ions (A/q3) Heavy ions (A/q>3) | mA mA | 2 0.5
Pulse repetition rate | Hz | up to 10
Pulse length Light ions (A/q3) Heavy ions (A/q>3) | ms ms | 0.5 0.25
Max. pulsed beam power | kW | 260
# of QWR cryomodules |  | 3
# of HWR cryomodules |  | 2
Total length | m | ~55
Talk M. Mustapha

## Slide 12: Ion Injector: Smaller Racetrack Booster
Hexagon Pre-booster
Circumference: 120 m
KE: 3 GeV
Talk M. Mustapha
Single booster option
Circumf.: 180 m
KE: 8 GeV
Polarization: good
Pol. Deuterons: yes
Talk A. Kondratenko
Ion injection/formation scheme
Talk J. Guo
Step 2. Accumulating coasting beam
Step 3. Capture to bucket
Step 4/5. Cool and accelerate to 7.9GeV
Step 6. Bunch compression
DC cooler
BB cooler
BB cooler
DC cooler
Step 7/8. Bucket-to-bucket transfer to the collider ring, repeat 9 (above) or 27 (below) times

## Slide 13: e-ring emittance
The adoption of PEP-II lattice and magnets is cost effective but limits lumi performance because of large emittance .
Investigated several options to reduce emaittance
  Optimizing the optics in a couple of sections
  Adding (dipole) damping wigglers in the straight
  Offsetting the beam in quads (~7 to 8 mm)
  New magnets (instead of PEP-II magnets) but sill FODO cell arcs
  Different types of arc cell, such as DBA, TME
She will show that “optimizing the optics in a couple of sections” already gives ~30% emittance reduction, at the cost of ~110m added length
Baseline
Dipole set
Dipole set
2nd sol. + decoupling quads
1st sol. + decoupling quads
New
Dipole set
Dipole set
2nd sol. + decoupling quads
1st sol. + decoupling quads
Talk F. Lin

## Slide 14: e-ring spin tracking
Spin tune scan for the electron beam at 5 GeV is performed based on a Monte-Carlo simulation. The result shows the polarization lifetime is about 8 hours at 5 GeV, and more important, a figure-8 shape MEIC collider ring has no synchrotron sideband resonances.
Continuous injection is not in the baseline design, but should be (re)considered to reach an even higher average polarization.
IP
Spin Rotator
e-
Magnetic field
Polarization
Spin tuning solenoid
Talk F. Lin

## Slide 15: Beam Synchronization
Issue: energy-dependence of ion velocity desynchronizes ions with electrons
Explored various options without and in combination with harmonic jump
  Moving ion orbit
  Moving electron orbit and RF adjustment
  Scanning synchronization
Considered engineering implications
Proposed baseline
  Harmonic jump (to be demonstrated in simulations)
  Adjusting electron path length using a movable chicane
Conclusions
  Moving magnets is feasible: 10-15 shifts by a 3-person crew
  Frequency adjustment is within tuning range
x = 44 cm
x = -50 cm
Total bending angle and z length are fixed
Talk V. Morozov

## Slide 16: Nonlinear Dynamics: Ion Ring
Explored multiple compensation schemes  –I sextupoles pairs in the arcs
  Compensate chromatic smear at the IP
  Compensate residual linear chromaticity with additional sextupoles
(- 8p/p , + 13p/p)
At p/p = 0.3%
(- 40x , + 40x)
(- 40y , + 40y)
IP
talks by Y. Nosochkov, M.-H. Wang, G. Wei

## Slide 17: Ion Polarization
Figure-8 design
  Zero spin tune independent of energy: spin precession in one arc is cancelled in the other
  Spin control and stabilization with small solenoids or other compact spin rotators
Spin tracking in progress
  figure-8 with an error
2 T  2 m control solenoids can stabilize proton and deuteron spins up to 100 GeV
no stabilization
stabilization by 1 solenoid
Talk A.Kondratenko

## Slide 18: Cooler specs and challenges
Energy 20-55 MeV
Charge 420 pC
Repetition rate 476 MHz
rms Bunch length 70 psec
rms emittance 30 mm-mrad
rms Energy spread (uncorr.)* 3x10-4
Energy spread (p-p corr.)* <2x10-3
Solenoid field 2 T
Solenoid length 30 m
Injector Magnetized
Have to run very high current
  Must have energy recovery or cost is too high
  Also need SRF cavities but this means no magnetic fields in the cavities.
The current varies with position in the micro-bunch so space charge forces vary and cannot be perfectly compensated.
Any realistic design must bend the beam with discreet magnet elements.
No micro-pulsed high current source has been demonstrated
Bunch is very long in the cooler solenoid.
Talk S. Bensen
So…what’s so hard about that?

## Slide 19: Architectures: Traditional ERL and Linac-2-Linac
Same-cell energy recovery
Bends
Possible R2F/F2R with space charge
Dump energy
No merger
Up and down are linked in the same way
as traditional ERL
Bend happens after the cooling solenoid
May need bends for bunch stretcher
Cavity phasing and positioning important

## Slide 20: Status of the Super-ferric Magnet R&D
JLab has contracted TAMU to develop a 1.2m superferric model dipole
Deliverable 1 – Concept Design – COMPLETE
Deliverable 2 – Prototype Cable-In-Conduit winding – In Process, due at the end of CY’15
SF Dipole – With and Without Coil Supports
Talks P. McIntyre
T. Michalski

## Slide 21: Cabling techniques
NbTi Rutherford cable NbTi Cable-in-Conduit
Pros: Uses mature cable technology (LHC). Semi-rigid cable makes simpler end winding.
Semi-rigid round cable can be precisely located.
Cryogenics contained within cable.
Cons: Ends tricky to support axial forces. Cable requires development and validation.
Entire cold mass is a He vessel.

## Slide 22
Source for Magnetized Cooling
Talk R. Suleiman
Bunch length | 100 ps (3 cm)
Repetition rate | 476 MHz
Bunch charge | 420 pC
Peak current | 4.2 A
Average current | 200 mA
Transverse normalized emittance | 10s microns
 | 3 mm
Solenoid field at cathode (Bz) | 2 kG
Proposal awarded
2016 LDRD

## Slide 23: SRF R&D: e-ring RF design
Re-use proven PEP-II RF stations
476 MHz HOM damped 1-cell cavities
  34 cavities available
1.2 MW klystrons, 13 available
  Including power supplies etc.
Current limited by synch. rad. power at high energy, impedance at low energy
Synchrotron power limited
Impedance limited
nominal
PEP-II RF cavity
PEP-II Cavities in the SLAC tunnel
1.2 MW Klystron
2 MVA HVPS
Talk R. Rimmer

## Slide 24: SRF R&D: ion-ring RF design
952.6 MHz HOM damped 1-cell cavities, modular JLab type cryomodule
  High frequency/high voltage for short bunch (re-bucket at energy)
  Double repetition rate for future luminosity upgrade
952.6 MHz single cell 4-seater CM (~4.3m flange to flange)
New HOM damped cavity concept

## Slide 25: SRF R&D: Crab cavity
Design by ODU (A. Castilla Ph.D project)
952.6 MHz “RF dipole” like LHC
Modest RF system (no beam loading)
Must have good HOM damping
Count for 1 IP in baseline
Assume cryostat cost/cavity same as ion storage ring
Talks J. Delayen
A. Castilla

## Slide 26: MEIC Civil: site planning
1
3
2
4
5
9
7
14
6
8
10
13
12
11
cs1
cs2
cs3
cs4
cs5
cs6
cs7
cs8
cs9
cs10
cs11
et1
cs14
cs15
cs17
cs18
cs19
cs20
cs21
cs22
cs23
cs24
cs13
cs12
cs16
et2
et3
et4
et5
15
Talk R. Yasky

## Slide 27: Conclusion
The accelerator program is progressing well:
Solid baseline and first pass cost estimate
Plan for FY16-17 in place
Ongoing baseline design improvements
Critical R&D initiated
Progress on critical issues:
synchronization, beam stripping and formation, spin tracking, beam-beam and collective effects, cooler design and cooling simulations
Started engineering, civil and ESH&Q activities
I will discuss future plans and priorities in my closing talk