## Slide 1: MEIC Ion Bunch Splitting
Defining the Problem
  Beam definition and bunch structure
  Operability and machine constraints
Possible Approaches
  Debunch/rebunch
  Adiabatic bunch splitting
  RF modulation gymnastics
  FEL-like microbunching
Plans and Path Forward
Todd Satogata (Jefferson Lab/ODU) and Randika Gamage (ODU)

## Slide 2: Defining the Problem: Parameters
Starting with ArXiV “MEIC Design Summary” parameters
  Table 7.1: αC=6.45e-3, γtr=12.46 => phase slip ηtr=6.362e-3
  Table 3.2: Collisions occur with 6.6e9 p/bunch with 1cm (33 ps) rms bunch length
    rms bunch length is ~1/30 of h=6832 bucket length
    Bucket area: A=0.223 eV-s, (dp/p)max=1.67e-3
    Bunch longitudinal emittance: εL≅7e-3 eV-s!
    Perfect adiabatic splitting: h=9 bunches: εL≅5.4 eV-s!

## Slide 3: Defining the Problem: Operability
Bunch splitting constraints
  Protect superconducting magnets from sudden beam losses
    Maintain at least one abort gap (of undetermined length)
    Barrier buckets or resonant gap clearing/collimation
  Impedance budget must be reasonable
    Splitting must be consistent with impedance model
    Impedance sources: SRF, BPMs, kickers, beam pipe transitions
  RF control loop constraints
    Beam loading at first seems insignificant
    But still possibly concern with low voltage, fine phase control
  RF costs and complexity
    Some scenarios require 7+ different RF frequencies!
    Harmonic cavity/control options?
  Final bunch distribution should be “even”
    Bunch intensity variation among final bunches should be small

## Slide 4: Approach 1: Debunch/Rebunch (Conservative)
Debunch beam completely and rebunch into higher harmonic
  Only two RF frequencies needed! ✓
  “Adiabatic” if RF voltages are changed on timescales much longer than synchrotron periods
    “long” times of small RF voltage: beam loading?
  Coasting beam instabilities ✗
    major concern of this approach
    Tradeoff cavity impedance/RF control vs non-adiabatic emittance growth
  Only one final spin orientation ✗
  Needs theory/simulations
1 AGS revolution period
24 bunches
Debunched beam
4 bunches
T. Roser, Transversity Workshop, Sep 2000

## Slide 5: Approach 2: Adiabatic Bunch Splitting (Conservative)
Split bunches successively
  “Adiabatic” if RF voltages are changed on timescales much longer than synchrotron periods
    Voltages must be carefully matched
    ~Doubles with every 2:1 split
  Reversible: bunch merging
  Requires many RF frequencies ✗
  Few instability/impedance concerns ✓
  Can also perform 1:n splits/merges ✓
    Higher than 1:2 require many harmonics, hard to operate reliably
    1:2 splits are reliable, well-understood
  Initial bunches can be different spin orientations ✓
K. Gardner, CA-AP 460, 2012
AGS 2:1 / 2:1 Bunch Merge

## Slide 6: Approach 2: Adiabatic Bunch Splitting
Randy and I have been working with longitudinal simulations in elegant (a code we’re both familiar with)
  But it’s not very effective for longitudinal dynamics of this sort
    Strong dependency on time coordinate, RF phasing, slow 6D tracking
Shifting towards putting parameter set into ESME
  Fermilab longitudinal dynamics (only) code: faster, longitudinally oriented
PS bunch merge animation from ESME base distribution (plus some postprocessing for movie)

## Slide 7: Possible Choices of Nh
Nh |  | 3600 |  |  | 3584 |  | 
Circumference (m) |  | 2266 |  |  | 2256 |  | 
Nh0 |  | 16 | 30 | 40 | 16 | 28 | 32
Occupied long bunches |  | 14 | 28 | 36 | 14 | 26 | 30
Gap length (ns, ×2) |  | 472 | 252 | 378 | 470 | 269 | 235
Linac Energy (MeV/u) | Pb | 100 | 55 | 42 | 100 | 57 | 50
 | Proton | 215 | 125 | 100 | 215 | 130 | 115
Occupied short bunches |  | 3150 | 3360 | 3240 | 3136 | 3328 | 3360
Split scheme |  | ×3×3×5×5 | ×5×4×3×2 | ×5×3×3×2 | ×7×25 | ×27 | ×7×24
Plenty of options to reduce bunch reprate
Binary split, might be the easiest
Factor of 7 split, might be beneficial for e-ring injection with reduced reprate
~110m longer than 2154m, just enough for the bypass lines
J. Guo, MEIC Weekly

## Slide 8: Approach 2: Adiabatic Bunch Splitting
This many bunch splits/merges is unprecedented
A “simple” 2n scheme is conservative and workable
But it still has challenges
  Naïve ratio of RF voltages is 1:2 with each step, or over two orders of magnitude in total
  Many RF voltages: multiplicity of expense, impedances
  Bunch splitting must be performed with barrier bucket
  Every split will not be perfectly adiabatic
    Determine workable initial parameter set
    Evaluate final bunch quality sensitivities to errors
    Evaluate impact on project costing, impedance budget

## Slide 9: Approach 3: RF Modulation (Liberal)
Create resonances in longitudinal phase space with RF phase/voltage modulation
  Devised to “mine” particles from core to high momentum for parasitic extraction
  A different type of bunch splitting
    Could also envision “reverse slip stacking” or “reverse muon coalescing”
  Does not need full spectrum of RF cavities ✓
  Never investigated for bunch splitting ✗
  Biggest challenges:
    Even bunch distribution in split bunches
    RF phase/frequency modulation control
    Linear 90 degree bunch rotation
      Adiabatic phase shift?
    Likely requires big momentum aperture
RF Nonlinear Resonance Island
S. Peggs, Proton Mining, FNAL AP-91-001
5-1 split after 90° phase rotation

## Slide 10: Approaches 4: FEL Microbunching (Very Liberal)
“Single long bunches becoming many short bunches” happens in other places:
  Electron beams in SASE FELs
  Bunching potential exponentially created by FEL beam
  Could one substitute many passes through an intense laser for reduction in laser intensity, increased beam rigidity vs FEL?
    Or create a controlled impedance-driven coherent instability that drives bunching
Crazy? Probably…
  Discussions with S. Webb (Radiabeam) and C. Prior (ASTeC)
  Use RF modulation methods to distribute RF bucket evenly
  Evaluate near transition first where there is no RF slip (but high sensitivity to driving impedances)

## Slide 11: Plans and Path Forward
The MEIC ion bunch splitting problem is interesting!
  Split h=9 to h=6832 beam with barrier buckets, no cooling
  Even bunch distribution, multiple polarization orientations
  Worthy breadth of topics to finish R. Gamage’s PhD thesis
The MEIC ion bunch splitting problem is challenging!
  Classical debunch/rebunch is likely infeasible (instabilities)
  Adiabatic bunch splitting is likely feasible but expensive (lots of RF)
    Simulate with esme rather than elegant, define parameter space
    Parameter sensitivity studies must be done
    1:2 splits are much easier to control than other splits
  Other research-oriented approaches are being investigated
    Longitudinal nonlinear bunch splitting (proton mining)
    Controlled FEL-like microbunching