## Slide 1: Interaction Region Backgrounds
M. Sullivan
for the
MEIC Collaboration Meeting
Oct. 5-7, 2015

## Slide 2: Outline
Brief Introduction
Synchrotron Radiation backgrounds
Beam-Gas-Bremsstrahlung
Luminosity backgrounds
Wake-field and Higher-Order-Mode Power
Summary
Conclusion

## Slide 3: Electron IR Parameters
Electron beam
  Energy range 3-10 GeV
  Current (5/10 GeV) 3/0.7 A
  Beam-stay-clear 12 beam sigmas
  Emittance (x/y) (5 GeV) (14/2.8) nm-rad
  Emittance (x/y) (10 GeV) (56/11) nm-rad
  Betas
    x* = 10 cm x max = 300 m
    y* = 2 cm y max = 325 m
Final focus magnets
  Name Z of face L (m) k G (10 GeV-T/m)
  QFF1 2.4 0.7 -1.3163 -43.906
  QFF2 3.2 0.7 1.3644 45.511
  QFFL 4.4 0.5 -0.4905 -16.362

## Slide 4: Ion IR Parameters
Proton/ion beam
  Energy range 20-100 GeV
  Beam-stay-clear 12 beam sigmas
  Emittance (x/y) (60 GeV) (5.5/1.1) nm-rad
  Betas
    x* = 10 cm x max = 2195 m
    y* = 2 cm y max = 2580 m
Final focus magnets
  Name Z of face L (m) k G (60 GeV)
  QFF1 7.0 1.0 -0.3576 -71.570
  QFF2 9.0 1.0 0.3192 63.884
  QFFL 11.0 1.0 -0.2000 -40.02

## Slide 5: IR Layout
EM Calorimeter
Hadron Calorimeter
Muon Detector
EM Calorimeter
Solenoid yoke + Hadronic Calorimeter
Solenoid yoke + Muon Detector
HTCC
RICH
RICH
Tracking
5 m solenoid
IP
Ultra forward
hadron detection
dipole
dipole
Low-Q2
electron detection
Large aperture
electron quads
Small diameter
electron quads
ion quads
Small angle
hadron detection
dipole
Central detector with endcaps
~50 mrad crossing
Courtesy
Pawel Nadel-Tournski and Alex Bogacz

## Slide 6: SR backgrounds
We need to check background rates for various electron machine designs
The 5 GeV e- design has the highest beam current
The 10 GeV design has the highest photon energies and largest beam emittance

## Slide 7: SR for 5 GeV (3 A)
Photons/crossing >10 keV

## Slide 8: SR for 10 GeV (0.7 A)
Numbers are Watts
Photons/crossing >10 keV
Beam pipe design fits 10 beam envelope. Prefer larger.

## Slide 9: 10 GeV (0.7 A) with tighter mask
Photons >10 keV/crossing
Numbers are Watts

## Slide 10: SR results
Difficult to get an IR beam pipe much smaller than a 3cm radius in X. Y is better.
  Need to see how many photons penetrate the beam pipe and make a hit in the first inner detector
Need to know how long the central pipe needs to be
  Shorter pipes are easier to shield
For the 10 GeV case the masking is tight
  This is probably a problem for BGB backgrounds (next topic)

## Slide 11: BGB, Coulomb, etc.
There are several processes that enter here:
  Electron – gas molecule inelastic collision (BGB)
  Electron – gas molecule elastic collision (Coulomb)
  Ion – gas molecule nuclear collision (Inelastic)
  Ion – gas molecule elastic collision (Coulomb)
The elastic collisions tend to produce a halo (or tail) distribution around the beam
  Need to track these collisions around a much larger part of the ring (perhaps the entire ring)

## Slide 12: Electron – gas molecule
BGB – Electron-gas inelastic collision
Result is a high energy gamma and a very off-energy electron beam particle
Coulomb – Electron-gas elastic collision
Result is an on-energy electron beam particle but with a large scattering angle

## Slide 13: Ion – gas molecule
Ion-gas nuclear collision
Result is a mess with probably all particles lost locally
Ion-gas elastic collision
Result is an on-energy ion beam particle but with a large scattering angle

## Slide 14: More on BGB, etc.
I think the nuclear collisions between ion and gas molecule will vanish from the machine close to the location of the collision point
The elastic ion – molecule collision will probably also produce a halo around the ion beam but this we should be able to collimate away

## Slide 15: Program Decay Turtle
This program can be used to track the off-energy beam particles and the produced gammas from BGB as well as the Coulomb scattered beam particles
  I have an old FORTRAN version
Uses an input deck with as much of the beam line as you want to install
Collimators are essential but collimating much closer than about 7 will probably start to lower the electron beam lifetime
  If a collimator starts to affect the beam lifetime then that collimator becomes a big source of local backgrounds

## Slide 16: Luminosity backgrounds
Luminosity backgrounds include:
  eP bremsstrahlung (also lumi signal and low Q2 data)
  Off-energy electron beam particles from above (also low Q2 data)
    > MHz data rate
  eP  eeeP (two photon electron pair production)
    The very low energy e+e- pair curl up in the detector field and make multiple hits in the vertex tracker
These will need to be checked to make sure they are under control or are not an issue

## Slide 17: Wake-fields and HOMs
HOM power and wake fields mostly come from the electron beam and travel up (and down) the electron beam pipe and the proton beam pipe
  It comes from the shared IP beam pipe
The proton beam does not generate nearly as much HOM power as the electron beam mainly because of the low gamma
  Still needs to be checked for beam pipes that have cavities. Low power can still melt vacuum elements.

## Slide 18: We estimate that a few Watts did this
This RF seal was suppose to seal off HOM power from getting between two vacuum flanges that had some amount of internal flex
3/8” SS washer melted
The seal frame was SS and was bolted to water cooled Cu
Vaporized and melted Cu RF seal
Cu melts at 1357
Vaporizes at 2840
Fe melts at 1808
HER beam 1.5-1.8 A

## Slide 19: Wake field simulation
With permission from Sasha Novokhatski, I have the following slide show of what the fields of a beam bunch do as the bunch travels through the PEP-II IR shared beam pipe

## Slide 20: PEP-II IR

## Slide 21: 2001 Calculations

## Slide 36: Summary
There are several background sources that need to be studied
We need to make sure all of the sources are under control
Backgrounds can change as the IR design evolves
We need to continue to check the background sources

## Slide 37: Conclusions
SR looks under control but needs further study
BGB backgrounds need to be checked
Luminosity backgrounds should be calculated
HOM effects will need to be estimated
Lots to do…