## Slide 1
S.A. Veitzer
High-Performance Modeling of Electron Cloud Effect and RF Diagnostics
MEIC Collaboration Meeting
JLAB, October 6, 2015
This work was performed under the auspices of the Department of Energy as part of the ComPASS SCiDAC-2 project (DE-FC02-07ER41499), and the SCiDAC-3 project (DE-SC0008920). Additional support from the Department of Energy, HEP division through the SBIR program.

## Slide 2: Electron Cloud Effect (ECE) Can Limit Accelerator Performance
What is the ECE?
  Primary electrons are accelerated by the beam potential to beam pipe walls as successive bunches cross
  Secondary electrons are produced with low energy at the walls, and are then accelerated by the next bunch
  If the secondary electron yield > 1 then the electron cloud density increases
  The cloud dissipates during gaps in the bunch train

## Slide 3: Electron Cloud Effect (ECE) Can Limit Accelerator Performance
What is the ECE?
  Exists in both lepton and hadron circular accelerators
  Electron plasma buildup can interfere with beams
    Increase emittance
    Create beam instabilities
Primary electron production
  Beam scrape-off
  Synchrotron radiation
  Residual neutral gas ionization
Secondary electron production
  Acceleration of electrons by beam potential to opposite beam pipe walls
  Resonant behavior (similar to multipacting)
    Depends on the bunch spacing, current, magnetic fields, and physical dimensions of the beam pipe
Three regimes: Buildup, Saturation, Dissipation
magnetic fields are important
  Electrons can become trapped, e.g. quadrupole magnets
  Solenoidal B can confine electrons near beam pipe edges
  Dipole B affects electron trajectories
There are a variety of mitigation techniques
  Surface coatings (lower SEY)
  Solenoidal fields (confine electrons near beam pipe walls)
  Surface grooving
  Modified bunch spacing

## Slide 4: Computational PIC Requirements
Electrons are non-relativistic
  So electrostatic models are accurate
  Typically very little along-beam motion, so 2D models are useful, usually
There exists a natural separation of scales, that makes modeling difficult
  Electron motions and cloud modulation by bunch crossings is on the order of bucket time
  Collective effects and bunch instabilities are on the order of revolution time scales.
There are a number of PIC simulation codes that have been used to model ECE
  WARP+POSINST
  ECLOUD
  VORPAL
  +
In general, requires
  Parallel computation; electrostatic solvers with domain decomposition
  Self-consistent particle evolution (space charge)
  Cut-cell algorithms for solution accuracy
  Ability to model externally applied magnetic fields
  Secondary electron surface and materials models
  Short time steps, long simulation times
MEIC parameters are in a regime that has not yet been modeled
  Long trains of high frequency buckets

## Slide 5: Buildup and Dissipation Simulations
Cloud buildup is fast
Saturation at some large fraction of linear beam charge
Dissipation during gap in bunch train
We can model electron cloud survival rate
Model effect of low-charge trailing bunch on cloud survival rate
Veitzer & Stoltz, Electron Cloud Buildup and Dissipation Models for PIP-II, IPAC’15, MOPMA037

## Slide 6: RF Diagnostic Modeling
Injected RF energy is affected by ecloud modulation
The ecloud plasma changes the dispersion relation, modulation of ecloud density can be measured experimentally
  Phase shift if frf > fcutoff
  Frequency shift if frf < fcutoff
Phase shift is proportional to cloud density
In spectral measurements, the side band
amplitudes are also (ideally) linearly related
to cloud density
N. Eddy, Project X Collaboration Meeting, 2009
Veitzer, Smithe, Application of New Simulation Algorithms for Modeling RF Diagnostics of Electron Clouds, AAC’12

## Slide 7: RF Diagnostic Modeling
Magnetic fields play a large role in cloud evolution
Plasma dielectric models can predict phase shifts for different B configurations
Veitzer, Vorpal Simulations Of Traveling Wave RF In Wiggler Magnetic Fields, ECLOUD’12

## Slide 8: Traveling RF Diagnostic Modeling
Perform buildup simulations for one revolution, including dissipation (2 ms)
Derived dielectric tensor from time-dependent cloud density (magnetized)
Perform dielectric simulations of RF propagation for many revolutions
  Field updates only, stable for long simulation times
  No particle noise (grid heating)
Measure side-bands due to modulation of electron plasma
Veitzer, Stoltz, Lebrun, Integrated Kinetic And Plasma Dielectric Models of Electron Cloud Buildup And TE Wave Transmission, NAPAC’14, MOPBA24

## Slide 9: Traveling RF Diagnostic Modeling
Perform buildup simulations for one revolution, including dissipation (2 ms)
Derived dielectric tensor from time-dependent cloud density (magnetized)
Perform dielectric simulations of RF propagation for many revolutions
  Field updates only, stable for long simulation times
  No particle noise (grid heating)
Measure side-bands due to modulation of electron plasma
Veitzer, Stoltz, Lebrun, Integrated Kinetic And Plasma Dielectric Models of Electron Cloud Buildup And TE Wave Transmission, NAPAC’14, MOPBA24
B=0
f = 1.5 fc
B=0.5 T dipole
f = 1.05 fc
Upper hybrid resonance

## Slide 10
This work was performed under the auspices of the Department of Energy as part of the ComPASS SCiDAC-2 project (DE-FC02-07ER41499), and the SCiDAC-3 project (DE-SC0008920)
Modeling rf Resonant Cavity Method For Measuring Electron Cloud Effect Using Plasma Dielectrics
The resonant cavity technique will reduce uncertainties in EC measurements due to rf attenuation and reflections
Perform detailed electrostatic PIC simulations to model plasma build-up and dissipation over one revolution period
Derive dielectric tensor strength from electron positions
Model rf injection below cutoff through time varying plasma dielectric over many thousands of revolution periods to measure sidebands
First attempt to numerically model the resonant cavity technique, and compute side bands due to EC modulation
Non-zero side band amplitude at same location as rf injection due to frequency modulation, as opposed to travelling-wave side bands, that are due to phase shifts
Numerically stable simulations with more than 40 million time steps using dielectric models, needed to resolve 500 kHz side bands, that are otherwise not possible with kinetic PIC codes due to grid heating
Linear increase in side band amplitudes as a function of distance from the rf source
Simulated spectrum showing side bands from frequency modulation, that are generated by harmonic modulation of electron cloud density (dielectric tensor)
Evanescent wave traps rf energy, providing localized sampling of electron cloud, creating a virtual resonant cavity
The resonant frequency of this cavity depends on the EC, via the dielectric strength, which is modulated by the beam
Seth A. Veitzer, David N. Smithe, Peter H. Stoltz, Tech-X Corp., Boulder, CO USA

## Slide 11: Conclusions
MEIC beam parameters are unique and the effect on electron cloud buildup is not known
Modeling of ECE for MEIC can be useful for aiding design to mitigate performance degradation
  Materials
  Bunch structure
  Magnetic field configurations
Focus is on both particle/surface interactions and modeling of cloud/beam collective effects
  Secondary electron processes
  Multipacting
  Beam instabilities
  ECloud-induced emittance growth and tune shifts
Addition of RF diagnostics to design may aid in assessing efficacy of ECE mitigation