## Slide 1
Alex Bogacz
MEIC Ion Injector Complex - Present Status

## Slide 2
MEIC Complex - Baseline Layout
IP
Future IP
Ion Sources
8 GeV Booster
Electron-Ion Collider
Rings
12 GeV CEBAF
5.5-pass CW RLA
Halls A, B, C
Electron Injector
Hall D
SRF Linac to 285 MeV
3-10 GeV
8 to100 GeV
3-10 GeV

## Slide 3: Ion Injector Complex - Overview
Present status of the ion injector complex:
  Relies on demonstrated technology for injectors and ion sources
  Adopted an SRF linac design (al FRIB)
  8 GeV Booster design avoiding transition crossing with all ion species
  Injection/extraction transfer lines to/from the Booster have been designed

## Slide 4: Evolution of Beam Parameters: Polarized Protons
 | (units) | *ABPIS Source | Linac | Booster | 
 |  |  | Entrance | Injection | Extraction
Charge status |  | H- | H- | H- ￫ H+ | H+
Kinetic energy | MeV | ~0 | 13.2 | 285 | 7062
g |  |  |  | 1.3 | 8.52
b |  |  |  | 0.64 | 0.993
Pulse current | mA | 2 | 2 | 2 | 
Pulse length | ms | 0.5 | 0.5 | 0.22 | 
Charge per pulse | μC | 1 | 1 | 0.44 | 
Protons per pulse | 1012 | 3.05 | 3.05 | 2.75 | 
Pulses |  |  |  | 1 | 
*ABPIS - Atomic Beam Polarized Ion Source

## Slide 5: Evolution of Beam Parameters: Ions (e.g. Pb)
 | (units) | *EBIS Source | Linac | Booster | 
 |  |  | After stripper | Injection | After acceleration
Charge status |  | 208Pb30+ | 208Pb67+ | 208Pb67+ | 208Pb67+
Kinetic energy | MeV/u | ~0 | 13.2 | 100 | 670
g |  |  |  | 1.11 | 1.71
b |  |  |  | 0.43 | 0.83
Pulse current | mA | 1.3 | 0.1 |  | 
Pulse length | ms | 0.01 | 0.01 |  | 
Charge per pulse | μC | 0.075 | 0.015 |  | 
Ions per pulse | 1010 | 1.0 | 0.2 |  | 
Pulses |  |  |  | 28 | 
* EBIS - Electron Beam Ion Source
Notes: Red box: RF frequency swing of heavy ions, no problems but must be paid attention to

## Slide 6: Ion Source Options
Ions | Source Type | Pulse Width | Rep. Rate | Pulsed Current | Ions/pulse | Polarization | Emittance (90%)
 |  | μs | Hz | mA | 1010 |  | π·μm·rad
H-/D- | ABPIS | 500 | 5 | 4 (10) | 1000 | > 90% | 1.0 / 1.8
H-/D- | ABPIS | 500 | 5 | 150 / 60 | 40000/15000 | 0 | 1.8
3He++ | ABPIS | 500 | 5 | 1 | 200 | 70% | 1
3He++ | EBIS | 10 - 40 | 5 | 1 | 5 (10) | 70% | 1
6Li+++ | ABPIS | 500 | 5 | 0.1 | 20 | 70% | 1
Pb30+ | EBIS | 10 | 5 | 1.3 (1.6) | 0.3 (0.5) | 0 | 1
Au32+ | EBIS | 10 - 40 | 5 | 1.4 (1.7) | 0.27 (0.34) | 0 | 1
Pb30+ | ECR | 500 | 5 | 0.5 | 0.5 (1) | 0 | 1
Au32+ | ECR | 500 | 5 | 10.5 | 0.4 (0.6) | 0 | 1
ABPIS - Atomic Beam Polarized Ion Source
EBIS - Electron Beam Ion Source
ECR - Electron Cyclotron Resonance
V. Dudnikov
6

## Slide 7: Warm/Cold Ion Linac - Current Baseline
Linac design based on the ANL linac for FRIB
  Pulsed linac capable of accelerating multiple charge ion species (H- to Pb67+)
Warm Linac Sections (115 MHz):
  RFQ (3 m)
  MEBT (3 m)
  IH structure (9 m)
Cold Linac Sections:
  QWR + QWR (24 m + 12 m) 115 MHz
  stripper, chicane (10 m) 115 MHz
  HWR section (60 m) 230 MHz
Ion species: p to Pb | 
Ion species for the reference design | 208Pb
Kinetic energy (p, Pb) | 285 MeV 100 MeV/u
Maximum pulse current: Light ions (A/Q<3) Heavy ions (A/Q>3) | 2 mA 0.5 mA
Pulse repetition rate | up to 10 Hz
Pulse length: Light ions (A/Q<3) Heavy ions (A/Q>3) | 0.50 ms 0.25 ms
Maximum beam pulsed power | 680 kW
Fundamental frequency | 115 MHz
Total length | 121 m
P. Ostroumov, ANL
Optimum stripping energy: 13 MeV/u
10 cryostats
4 cryostats
2
Ion Sources
QWR
QWR
HWR
IH
RFQ
MEBT
10 cryos
4 cryos
2 cryos
EBIS
ABPIS

## Slide 8: Warm RF Components
RFQ Segment
Frequency | 115 MHz
Total length | 3.6 m
Voltage | 85 kV
Average radius | 7 mm
Number of segments | 4
Input energy | 25 KeV
Output energy | 500 keV/u
IH Structure

## Slide 9: Superconducting Cavities
QWR HWR
P. Ostroumov, ANL

## Slide 10: Superconducting Ion Linac
Superconducting linac provides superior flexibility to maximize energies for multiple charge ion beams (from H- to 208Pb67+).
  SC linac can provide 100 MeV/u for lead ions.
  In the same SC linac, an H- beam can reach 280 MeV, which is high enough to suppress space-charge in the booster (space-charge is most severe for the lowest mass-to-charge ratio, i.e. H-)
  Single 2-gap SC cavity can provide significantly higher (factor of ~ 10) voltage per cavity compared to room temperature cavities. High-Q (power ~ voltage2) ⇨ much higher peak fields available with SC cavities.
P. Ostroumov, ANL

## Slide 11: Voltage Gain per SC Cavity – Final Energies
208Pb67+
H-
P. Ostroumov, ANL

## Slide 12: Ion Source/Linac – Space-Charge Issues
The space-charge effects are quite significant in the injection beam-lines from the ion sources.
  Emittance after both ABPIS and EBIS are not simple ellipses, beam collimation is required before transferring ions into the linac.
Following the RFQ there are no significant space-charge effects
  If EBIS is used for ion beam generation (peak current ~5 mA) one needs to compensate space charge defocussing with standard rms beam envelope matching technique.

## Slide 13: Booster (8 GeV, gt = 10)
injection
extraction
RF cavity
Crossing angle:
75 deg.
Injection: multi-turn 6D painting
  0.22-0.25 ms long pulses ~180 turns
  Proton single pulse charge stripping at 285 MeV
  Ion 28-pulse drag-and-cool stacking at ~100 MeV/u
  Ion energies scaled by mas-to-charge ratio to preserve magnetic rigidity
Ekin = 285 MeV – 7.062 GeV
Ring circumference: 273 m
(≈ 2200/8)
13
272.306
0
70
0
7
-7
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Straight
Inj. Arc (2550)
Straight (RF + extraction)
Arc (2550)
A. Bogacz

## Slide 14
Arc Quadrupoles:
Lq = 40 cm
G = 12-58 Tesla/m
Arc Bends:
Lb = 120 cm
B = 2.73 Tesla
bend ang. = 7.08 deg.
Sagitta =1.8 cm
Straight Quads:
Lq = 40 cm
GF = 12.57 Tesla/m
GD = -24.52 Tesla/m
GF = 12.57 Tesla/m
Booster Lattice (8 GeV, gt = 10)
A. Bogacz
Lattice configured with super-ferric magnets
14
272.306
0
70
0
7
-7
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y

## Slide 15: Ion Injection – Transverse Phase-space Painting
55
31.8
30
0
5
-5
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Doublet straight injection optics
separation of the injection orbit bump (12s)
B. Erdelyi, NIU

## Slide 16: Acceleration - Low Frequency RF Cavities
Booster |  |  |  |  |  | H+ |  |  | 208Pb67+ |  |  | 
Circumference |  | 273 | m |  | Energy | 0.28 | - | 8 | 0.112 | - | 3.2 | GeV
Harmonic Number |  | 1 |  |  | RF Frequency Range | 0.817 | - | 1.274 | 0.578 | - | 1.25 | MHz
Gaps per Cavity |  | 2 |  |  | Ramping Time |  |  | 0.396 |  |  | 0.56 | sec
Cavity Number |  | 1 |  |  | Vgap |  |  | 8.0 |  |  | 5.75 | kV
Cavity Length |  | 2.2 | m |  | Beam Power |  |  | 8.0 |  |  | 1.85 | kW
Total Cavity Length |  | 2.2 | m |  | Power Loss per Cavity |  |  | 41.2 |  |  | 41.2 | kW
Ferrite Toroid Inner Radius |  | 0.25 | m |  | Syn. Phase |  |  | 30.0 |  |  |  | 
Ferrite Toroid Outer Radius |  | 0.5 | m |  |  |  |  |  |  |  |  | 
Ferrite Stack Length |  | 1 | m |  | Acceleration time |  |  | 120 |  |  | 144 | msec
Maximum Vgap |  | 10 | kV |  | Cooling time |  |  | 16 |  |  | 55 | msec
S. Wang
16

## Slide 17: Booster - Space-Charge Issues
Incoherent space-charge tune shift at injection (285 MeV):
  Present baseline: DQsc = 0.1 (for 0.2 Amp coasting beam)
  Consider more aggressive scenario … DQsc ≥ 0.3
Structure resonance crossing and stop-band corrections
  Significant fraction of particles in the beam can move cross third-integer and quarter-integer resonance lines.
  Properly placed quadrupoles and sextupoles could be used to correct the stop-band width of those resonances to minimize the amplitude growth and hence the beam loss.
Halo generation ⇨ beam collimation required
G. Franchetti
FAIR
I. Hofmann
GSI

## Slide 18: Large Space-Charge Tune Shift Operation
S. Gilardoni CERN
PS Booster at CERN
tune scan

## Slide 19: Tune Diagram – Space-charge Footprint?
272.306
0
70
0
7
-7
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
10
9.5
9
8.5
5
4
3
2
Table 1 Dipole, multipoles in units of 10-4, reference radius at 1.5 cm
Table 2 Quad multipoles, reference radius 3 cm
Qx/y = 9.87 / 8.85
Nominal current 15kA (Iscale=1)
Tracking for 1.2×105 turns
Qy
Qx
P. McIntyre
Texas A&M

## Slide 20: Linac-to-Booster Transfer Line
Booster injection scheme
  Combined longitudinal and transverse phase space painting
  Components: stripping foil, four-dipole booster orbit bumper system, magnetic and electrostatic septa
Two same-strength quadrupole families of opposite sign
  Eighteen 16 T/m 20/30 cm magnetic/physical length quadrupoles
  Each quadrupole surrounded by 30 cm long corrector and 15 cm long BPM
  Enough quadrupoles for matching to linac and booster as needed
Achromatic 1 m vertical step
  Two 0.5 T 50/78 cm magnetic/physical length dipoles
matching
ions
vertical step
matching
V. Morozov

## Slide 21
Booster-to-Ion Ring Transfer Line
83.8917
0
50
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
kicker
127.50 Arc
kicker
septum
septum
Lattice based on FODO (900 )
5.5
0
2
-2
Coordinates X&Y[cm]
X
Y
Kickers (2):
L[cm] 120
B[kG] 1.5 angle [mrad] 5
Rise time [ns] Flat Top [ns] Fall time [ns]
300 300 300
Horizontal Extraction: Kicker + Septum
A. Bogacz
  Enough independent quadrupoles (8) for betatron matching to Ion Ring
Booster Extraction
Ion Ring
Injection
21

## Slide 22: Summary
The MEIC hadron injector complex design is well established
Present choice for Ion Sources:
  ABPIS for polarized protons and light ions
  EBIS for un-polarized heavy ions
SRF Linac based on FRIB (285 MeV protons and 100MeV/u lead)
8 GeV Booster design avoiding transition crossing (including transfer lines)
  Low momentum compaction Optics based on perturbed FODO lattice
  Lattice configured with super-ferric magnets (Texas A&M design)
  Injection: Combined longitudinal and transverse phase-space painting
  Extraction: Single kicker and magnetic septum
  Space-charge tune ‘footprint’ needs to be studied in the presence of multipoles
No clearly identified technical risks present
Proven, conservative technologies used throughout the scheme

## Slide 23: Backup Slides

## Slide 24: Medium Energy Beam Transport (MEBT)
Q1
Q3
Q2
Q4
Buncher
L= 995 mm
 | Eff. Length (mm) | Gradient (T/m)
Q1 | 20.0 | 23.0
Q2 | 50.0 | -22.0
Q3 | 50.0 | 32.75
Q4 | 50.0 | -16.5
Quadrupole Parameters
Cavity | Quarter Wave
Voltage | 0.8 MV
Frequency | 115 MHz
Length | 340 mm
Buncher Parameters
Space-charge defocusing significant - rms beam envelope matching required
y
x
x’
DW/W
Df
y’
y
x
x’
DW/W
Df
y’

## Slide 25: Stripping energy
208Pb30+  208Pb67+
P. Ostroumov, ANL

## Slide 26
P. McIntyre
Texas A&M
8.76306
0
30
0
3
0
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Bend:
Lb = 120 cm (magnetic length)
Lead ends: 2×22 cm
B = 2.73 Tesla
bend ang. = 7.08 deg.
Sagitta =1.8 cm
Bend
Sextupole
Bend
Sextupole:
Ls = 10 cm
S = 750 Tesla/m2
Correctors
BPM
Quad
Quadrupole:
Lq = 40 cm
G = 12-58 Tesla/m
Correctors (H/V): 10 cm
BPM can: 10 cm
Dual-dipole
Quad
Half-cell cryomodule
Arc Cell - Super-ferric Magnets
Magnet aperture radius:
6srms = 42 mm
26

## Slide 27: Adiabatic Capture and Acceleration (h =1)
protons
lead ions
B. Erdelyi, NIU
 | H+ |  |  | 208Pb67+ |  |  | 
Energy | 0.28 | - | 8 | 0.112 | - | 3.2 | GeV
RF Frequency Range | 0.817 | - | 1.274 | 0.578 | - | 1.25 | MHz
Ramping Time |  |  | 0.396 |  |  | 0.56 | sec

## Slide 28
Booster-to-Ion Ring Transfer Line - Magnets
83.8917
0
50
0
6
-6
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
kicker
127.50 Arc
kicker
septum
septum
Lattice based on FODO (900 )
Arc Quadrs (17):
Lq = 40 cm
G = 10-25 Tesla/m
Arc Bends (28):
Lb = 120 cm
B = 1.89 Tesla
bend ang. = 4.9 deg.
sagitta = 1.3 cm
Magnetic Septa (2):
Lb = 150 cm
B = 1.5 Tesla
bend ang. = -4.9 deg.
Booster Extraction
Ion Ring Injection
Magnet aperture radius:
6srms = 16 mm
A. Bogacz
28

## Slide 29: Other Boosters - Tunes
  SNS Accumulator: 5.82 / 5.80
  SSC LEB: 11.65 / 11.60
  SPS: 1.82 / 2.72
  SPS Booster: 6.23 / 6.25
  J-PARC RCS: 6.45 / 6.42
  MEIC Booster: 9.87 / 8.85