## Slide 1: DTL Option for MEIC Ion Injection
Jiquan Guo, Haipeng Wang
Jlab
3/30/2015

## Slide 2: Hardron Linac: Typical Layout
Source
SRF elliptical cavities
Alveraz/IH/CH/CC DTL
SRF spoke or QWR/HWR
RFQ
~0.1MeV
0.5-5MeV
5-200MeV
80-300MeV
>300MeV
IH-DTL
CH-DTL
SRF CH-DTL
Elliptical (medium β)
SRF Spoke
Alveraz DTL
SRF HWR

## Slide 3: DTL Efficiency
G. Clemente, CARE-Note-2007-001-HIPPI
IH-DTLs are proven up to 8-10MeV/u
FAIR 70MeV proton linac CH-DTL is under commissioning, a heavy ion version of CH-DTL for up to 22MeV/u U38+ has been proposed
Other DTLs like CC-DTL work at higher energy.
DTL (Drift Tube Linac) is a multi-gap accelerator structure with very high R/Q/L at low β. Efficiency drops as β goes higher, especially for IH/CH structures
Phase of different gaps are synced by the particle’s drift time. The structures have fixed (or very narrow) β profile.
Will get same Ek/u for different particles; have to lower Vgap for lighter particles to match the β profile, but also result in higher current capability.
Typical SRF QWR has Zeff in the order of 1011-1012Ω, 3~4 order of magnitude better

## Slide 4: RF cavities: warm vs SRF
Ohm takes SRF
Carnot favors warm
Warm: Need multi-MW level RF power – major cost driver
SRF: Need to pump out both dynamic and static heat load at 0.1-0.3% efficiency
Warm RF can take the advantage of pulsed operation: increases efficiency with higher in-pulse beam loading, no Ohmic loss when pulse is off, reduces RF source cost and wall plug power

## Slide 5: Technology choice
High β Low β
SRF single/double gap
Warm multi-gap
Low beam current High current
CW operation Low duty cycle pulsed
Different particles w/ same Ek/q Different particles w/ same Ek/u
SRF multi-gap cavity is also an option for 0.1<β<0.5 CW operation.
Warm DTL allows focusing magnets inside or very close to the tanks, which is crucial for β<0.1 heavy ion acceleration.
Zeff /L for warm single/double gap structure is a little bit low, and the available RF sources with very low duty cycle in the frequency range of 0.1-0.4GHz cost too much per Wavg.

## Slide 6: RF cavities: warm vs SRF, example 1, β~0.2
Warm CH-DTL (Use Zeff of Tank 5 of FAIR p-linac, 325MHz, β=0.22-0.25) | SRF QWR (115MHz, 2 cavities)
L=1.52m, Veff=4MV (scaled from 6MV) | L in cryomodule~1.6m, Veff=4MV
Zeff cos2Φ=82MΩ | R/Q=509Ω*2, Q~109, Φ=20°, Zeff cos2Φ=9×1011 Ω/cav
Pcu,peak=195kW | PNb=9W, Pstatic=4W, Pcryo=4kW
Ib=50mA with 0.3ms pulse width, 5Hz, 0.15% beam duty cycle, RF pulse width 0.5ms | Ib=2.5mA with 6ms pulse width, 5Hz, 3% beam duty cycle, ~5% RF duty cycle
PRF FWD,peak ~ 440kW (assume 10% reflection with beam loading) | PRF FWD = 15kW (30% reflection due to microphonics etc.)
PRF FWD, avg= 1.1kW | 
Wall plug power ~3kW RF | Wall plug power: ~2kW cryo, 2kW RF with DC modulation (>30kW if use tubes w/o DC modulation)

## Slide 7: RF cavities: warm vs SRF, example 2, β~0.4
CC-DTL (Module 4 of CERN linac 4 CC-DTL, 352MHz, β=0.38-0.40, 80MeV/u) | SRF HWR (230MHz, 3 cavities)
L=2.6m, Veff=8MV | L in cryomodule~2.4m, Veff scale to 8MV
Zeff cos2Φ=100MΩ | R/Q=250Ω*2, Q~109, Φ=20°, Zeff cos2Φ=4.4×1011 Ω/cav
Pcu,peak=640kW | PNb=48W, Pstatic=6W, Pcryo=20kW
RF pulse width 1ms 25Hz, Ib=50mA with 0.8ms pulse width, 2% beam duty cycle | CW RF, CW beam 1mA
PRF FWD,peak ~ 1150kW (assume 10% reflection with beam loading) | PRF FWD, cw = 12kW (30% reflection due to microphonics etc.)
PRF FWD, avg= 29kW | 
Wall plug power ~70kW | Wall plug power ~50kW

## Slide 8: MEIC Booster Ring Injection Requirements
Ek/u: 30-50MeV for Pb64+#, 50-100MeV for H-
Ion source pulse width: up to 0.5ms
Ion source current: up to 150mA for non-polarized H-, 4mA for polarized H-, as low as 0.1mA for Li3+
Rep-rate: 5 Hz nominal, depends on the ramping/cooling cycle in the booster ring
Only need to inject once in every 3-8hr, ~10µC of charged particles per injection. Each injection should take <=0.5hr. With ~1mA pulsed current, the total linac beam duration will be 10-1000ms, depending on the beam loss factor, so the overall duty factor is 10-4-10-6. Duty factor during injection should be ~0.1% or less.
Most of the parameters appear to prefer warm DTL, unless a side program is considered, or the required energy changes significantly.
Need to carefully examine the cost and performance of both technologies, with the consideration of the newest development in ion source and booster ring
# Pb charge state depends on stripping energy, which will be chosen to minimize total accelerating voltage, depending on the final particle energy. Here assumes a stripping energy of ~10MeV/u

## Slide 9: A conceptual design of the DTL for H- and heavy ions
Ion sources
RFQ
MEBT
IH
CH3
CH1
CH2
Section | RFQ | IH | CH1 | CH2 | CH3 (future upgrade)
Lowest Q/A particle to accelerate | Pb30+ | Pb30+ | Pb64+ | H- | H-
Exit Ek (MeV/u) | 1.4 | 10 | 40 | 60 | 100
Exit β | 0.055 | 0.145 | 0.283 | 0.341 | 0.428
Max Veff (MV) | 10 | 60 | 98 | 20 | 40
RF source (available for now) | 108/162/176MHz tetrode, <=400kW peak/tank, |  | 325 or 352MHz Klystron, 2.8MW peak/tank, <5kW average, may upgrade to magnetron |  | 
Number of tanks |  | 4-5 | 4-5 | 1 | 2
Stripper
Total peak RF power (~0.1% duty factor): <20MW for 40MeV Pb/60MeV H-, ~25MW for 100MeV H-. RF system wall-plug power during injection will be ~100kW, depending on duty factor.
Average wall plug power will be in the order of 10s of kW, dominated by idle power of the tubes and other equipment.
Estimated direct cost for HPRF sources and modulators: ~$10M
Capable for >20mA peak current, 0.2-0.5ms pulse width, 5Hz

## Slide 10: Option 2: two DTL linacs sharing RF sources
Ion sources
RFQ
MEBT
IH
6 tank CHDTL
Stripper @10MeV
Total peak RF power (~0.1% duty factor): ~20MW for 50MeV Pb/120MeV H-.
Linac 2 can be built later as a future upgrade.
H- source
RFQ
MEBT
4 tank CH
CCDTL
Linac 1, 50MeV/u Pb64+ and H-
(and all other ions with q/a>1/3)
Linac 2, ~120MeV H-
6 klystrons, 325MHz, 2.8MW
IH?

## Slide 11: Compared to the truncated baseline SRF linac
Ion sources
RFQ
MEBT
IH
HWR
QWR1
QWR2
Section | RFQ | IH | QWR1 | QWR2 | HWR
Lowest Q/A particle to accelerate | Pb30+ | Pb30+ | Pb30+ | Pb64+ | Pb64+
Exit Pb Ek (MeV/u) | 1.4 | 4.8 | 10 | 17 | 30
Exit H Ek (MeV/u) | 1.4 | 4.8 | 35 | 55 | 95
Max Veff (MV) | 10 | 25 | 35 | 23 | 42
RF source | 115MHz tetrode, <=400kW peak/tank, |  | 115MHz, ~8kW/cav |  | 230MHz, ~10kW/cav
Number of cavities/tanks |  | 3 | 20 | 15 | 15
Stripper
RF power: ~2MW pulsed + ~400kW high duty cycle or CW for 30MeV Pb/95MeV H-
4K Heat load: ~275W (~100W static and ~175W dynamic), needs ~100kW wall plug power to cool, average wall plug power for cryo is ~35kW
Capable for 2mA peak current, 0.2-0.5ms pulse width, 5Hz

## Slide 12: Summary
The requirements of MEIC injection, especially the pulsed beam time structure, made warm DTL a very attractive option.
Some limitations exist for DTL structures, like fixed β profile, and degraded efficiency at higher energy, but won’t eliminate DTL’s advantage.
Further design and cost estimate for warm linac (and SRF linac) options is needed for final decision.