## Slide 1: Induction Cell Synchrotron for MEIC Ion Complex
S Wang, J Guo, R Rimmer, H Wang
3/30/2015
JLAB

## Slide 2: Contents
Why
Induction Cell in Accelerators
  Induction Cell and Induction Linac
  Induction synchrotron
    Barrier bucket
    Energy Ramping
  KEK experiments
MEIC Ion Complex with Induction Cell

## Slide 3: WHY
Induction cell synchrotron could provide:
Accelerate all species of ions with one synchrotron at lower energy for MEIC;
Provide more bunch charge because of the uniform longitudinal charge density profile when subject to space charge limit

## Slide 4: Induction Cell
Non-resonant structure, low impedance, works in pulsed mode.
The change of ﬂux in the magnetic core induces an axial electric ﬁeld, which is the acceleration ﬁeld and appears at the gap of the secondary loop,
The power supply cable and the acceleration module are considered as one transmission line ﬁlled with diﬀerent materials. Charged particles are accelerated by the voltage diﬀerence between the inner and outer conductor of the transmission line and travel inside the inner conductor.
Transformer Type (Earlier)
Transmission Line Type (Modern)
ASTRON-I, N. Christofilos, R. Hester, W. Lamb, D. Reagan, W. Sherwood,
and R. Wright, Rev. Sci. Instrum 35, 886 (1964).
Shaoheng Wang, J. Deng, “Acceleration modules in linear induction accelerators”, Chinese Physics C, Vol. 38, No. 5 (2014) 057005

## Slide 5: Resonant Ferrite Loaded Cavity and Pulsed Induction Cell
Induction cells use large hysteresis loop area to get large Volt-Second number
In revolution frequency variable accelerators, like proton booster, the resonant working point is varied by varying DC bias current, the relative permeability of the core is changed, so is the resonance frequency.

## Slide 6: Induction Linac
Induction cells are cascaded to form the induction linac.
Typical parameters:
Gradient: 0.25 MV/cell,
beam energy: 20 MeV,
beam current: 2~3 kA,
0.1~2 us pulse width
rep rate, single pulse or a couple of pulses
(for example, a burst of 3 pulses)

## Slide 7: Induction Synchrotron
The induction synchrotron concept for accelerating charged particles, was introduced by K.Takayama and his colleagues in 2000:
Induction cells are placed in synchrotron to replace RF cavities to provide
acceleration and barrier bucket.
Demonstrated using the KEK 12 GeV synchrotron at KEK.
Typical parameters:
Gradient: several kV/cell,
driving current: 20 A,
us pulse level pulse width
rep rate, upto around 1 MHz

## Slide 8: RF Cavity vs Induction Cell
Bucket in
phase space
Potential well
Confinement
Acceleration
Below transition
head
tail
+
Cell
set 1
Cell
set 2
head
tail
The potential well hints the uniform bunch charge density distribution

## Slide 9: Barrier Bucket (below transition)
tbb
tbb
tflat
Vbb
f1
-f1
f1+df
In Barrier Bucket region:
DE1
-DE1
-f1-df

## Slide 10: Barrier Bucket (below transition), con’t
Tflat
Tbb
Tflat
Tbb
(f1, DE1)
2.15 km ion ring of MEIC:
Ramping top, before rebunching,
b = 0.99996
h = -6.327e-3
E = 100 GeV
DE/E = 2e-4,
DE1= 20 MeV
H=1
If we let the BB depth to be 2 colliding bucket lengh (harmonic number = 6832) then
For given and , we have

## Slide 11: Synchrotron Oscillation Period
Tflat
Tbb
Tflat
Tbb
(f1, DE)
(-f1, -DE)

## Slide 12: Synchrotron Frequency
2.2 km ion ring of MEIC
b = 1
f0 = 139 kHz
h = -6.327e-3
f1 = 0.5*(0.95*2p)
DE/E = 2e-4
E = 100 GeV
Vbb = 43.2 kV
H=1

## Slide 13: Operation of Induction Cell Synchrotron
Phys. Rev. ST Accel. Beams 14, 071301 (2011)
Suitable to accelerate all ion species in large enrgy range
because of the tunable pulse firing timing

## Slide 14: KEP PS, Induction Cell, BB + Acc
A single 100 ns, 500 MeV, 0.3% momentum spread proton bunch is injected and captured by the barrier bucket created by the induction step-voltages, and accelerated to 6 GeV in the KEK proton synchrotron.
Proton bunch trapped by step barrier voltages before acceleration. Sky blue, bunch signal;
yellow, barrier voltage
The net Vbb magnitude of 1.8 kVx6=10.8 kV was sufﬁciently to accommodate the injected bunch.
Proton bunch in the middle of acceleration.
Sky blue, bunch signal;
yellow, barrier voltage;
purple, induction acceleration voltage
Four induction acceleration cells of an output voltage of 1.6 kV per cell were employed to get a total of 6.4 kV.
yellow, beam current (1012/div);
sky blue, bunch monitor signal ;
purple, gate pulse density vs time;
green, central beam position (DR) (10mm/div).
PRL 98, 054801 (2007)

## Slide 15: KEK Digital Accelerator
The KEK digital accelerator is a renovation of the former KEK 500 MeV Booster, the injector to the KEK 12GeV proton synchrotron.
RCS, ramping rate of 10 Hz,
Rev. frequency of 80 kHz to 3 MHz demonstrated
K.Takayama, IPAC’11
Phys. Rev. ST Accel. Beams 14, 071301 (2011)
The ion beam intensity acceptable at the injection stage is limited by space-charge effect

## Slide 16: Bunch Length Manipulation
Yellow:
Bunch intensity
Blue:
Barrier Bucket pulses

## Slide 17: Focusing-Free Transition Crossing
Beam intensity and the bunch length during the transition
normal transition crossing
with flattened rf wave.
5% drop
[(a) and (b)]: normal transition crossing
[(c) and (d)]: with flattened rf wave
In a RF bucket the bunch shape is remarkably deformed by an inherently nonadiabatic nature in the synchrotron oscillation in the vicinity of a transition energy.
Grifﬁn proposed to eliminate the ﬁeld gradient of the fundamental harmonic by imposing the 2nd or 3rd harmonics during the transition crossing. It has been demonstrated in the Fermilab Main Ring,
Phys. Rev. Lett., 96:134801–134804, 2006; Phys. Rev. E 55, 1028 (1997); Fermilab-tm-1734

## Slide 18: Hardwares
The Switching power supply (SPS), which modulates a DC voltage, is operated in a full bridge circuit. The single switching arm consists of MOSFETs connected in series, which enables high-frequency switching at 1 MHz with an output voltage of 2.5 kV and peak current of 20 A.
In induction cell, FINEMET has been employed as the magnetic core material to maintain a couple of us long pulse.
Phys. Rev. ST Accel. Beams 14, 071301 (2011)

## Slide 19: MEIC Booster Ring, more charge or lower injection energy
Because of longer bunch length and unform longitudianl line density profile, the linear density is dropped by a factor of 3 for same bunch charge compared with bunch hold by a RF bucket..
Space charge tune shift:
For same bunch charge:
Type | Energy |  | Bunch Charge
RF | 50 MeV | 0.3484 | Q
Induction Cell | 50 MeV | 0.3484 | 3Q
Induction Cell | 20 MeV | 0.2120 | 1.8Q
Induction Cell | 6.5 MeV | 0.1187 | 1.0Q
Type | Energy |  | Bunch Charge
RF | 50 MeV | 0.3484 | Q
Induction Cell | 50 MeV | 0.3484 | 3Q
Induction Cell | 20 MeV | 0.2120 | 1.8Q
Induction Cell | 6.5 MeV | 0.1187 | 1.0Q
Peak density ratio
Bunch length ratio
RF
IC

## Slide 20: Induction Synchrotron in Low Energy Section Scheme 1
As the booster, accept ions from linac, hold three times bunch charge, or three times faster to provide enough ions for collider ring
Ion source and a short linac produce a 50 MeV ion beam;
Inject into Induction Cell booster rapide cycling synchrotron;
Ramping and cooling;
Using barrier bucket to shorten bunch length before transfer to collider ring

## Slide 21: Induction Synchrotron in Low Energy Section Scheme 2
As a pre-booster, accept ions from a very short linac
Ion source and a short linac produce a 6.5 MeV ion beam;
Inject into Induction Cell booster rapide cycling synchrotron;
Ramping to 300 MeV and cooling;
Transfer to booster

## Slide 22: MEIC Ion Collider Ring
Induction Cell can also be used in collider ring,
To produce a longitudinally uniform beam and simplify the rebunching process;
Produce length variable gap;

## Slide 23: Instability Issue
Head-Tail
It is noted that Dp/p and ωs in the barrier bucket are not independent. In general, ωs in the barrier bucket is extremely small compared to that in the RF bucket, therefore, the growth rate in the barrier bucket is much smaller than that in the RF bucket.
Takayama K. “Induction Accelerators”

## Slide 24: The End
Thank you !

## Slide 25: Volt-Second Number of the Cell
The change of flux in the magnetic core induces an axial electric field, which is the acceleration field and appears at the gap of the secondary loop
V0: the voltage pulse amplitude
t : the voltage pulse width
DBm: magnetic core flux density
varying range
S: core cross section area

## Slide 26: KEK PS, Induction Acc + RF Bucket
A single 500 MeV proton bunch injected and captured in the RF bucket, was accelerated from 500 MeV to 8 GeV, including the transition crossing, for three cases
with induction acceleration
with induction deceleration
without induction acceleration

## Slide 27: KEK PS, Induction Barrier Bucket
The proton bunch is captured by the induction barrier voltages at an injection energy of 500 MeV, and survived for more than 450 ms. The induction step-barrier voltages create a shallow notch potential. A long barrier-voltage pulse-length was ensured so as to fully capture the injected bunch with a momentum spread of 0.4%.

## Slide 28: KEK-DA, various ions
Phys. Rev. ST Accel. Beams 17, 010101 (2014)

## Slide 29: Ramping
Production of conﬁnement and accelerating voltage pulses is controlled by FPGA gate signals for SPSs. The SPS generates a set of positive and negative pulses to prevent the saturation of cell magnetic cores.
The conﬁnement voltage is generated every turn, whereas the accelerating voltage is intermittently generated because of the limited capabilities of the induction acceleration system.
two induction cells produce
two sets of set/reset voltage pulses, where pulse height and length are ﬁxed to be 1 kV and 150 ns, respectively, and the time duration between the two sets is changed in proportion to the revolution period.

## Slide 30: MEIC Ion Collider Ring
Current Scheme:
Use 7 ferrite loaded low frequency (~1.2 MHz) cavities to accelerate protons from 8 GeV to 100 GeV in 12 seconds, harmonic number is 9;
Energy ramping;
Nine long bunches are debunched into coasting beam;
Rebuching into ~6800 bunches with 952 MHz SRF cavities for colliding
Abort gap production?
Uniformity of bunch charge of the ~6800 bunches?
Large emittace reproduced during rebunching process against cooling result?
====================================================
Suggested Scheme with Induction Cell:
One or two super bunch are formed at injection from booster;
Energy ramping;
Length-variable gap production;
Rebunching into ~6800 bunches with 952 MHz SRF cavities for colliding
Gap length is variable
Uniform bunch charge of the ~6800 bunches