## Slide 1: ESnet Overview
Jason Zurawski – zurawski@es.net
Science Engagement Engineer, ESnet
Lawrence Berkeley National Laboratory
Future Trends in Nuclear Physics Computing
March 18th 2016

## Slide 4: ESnet Background
ESnet is a special-purpose mission network, funded by the US Congress to support scientific goals of the Department of Energy.
We see networking as a means to an end: scientific productivity.
We aim to create a world in which discovery is unconstrained by geography.

## Slide 5
This is not an ISP.

## Slide 6
It’s a DOE user facility designed to overcome the constraints of geography.
We do this by offering unique capabilities and optimizing the facility for data acquisition, data placement, data sharing, data mobility.

## Slide 7
Why?
Immediate driver: more capacity for LHC Run 2. But the extension supports all DOE missions, reducing barriers to European collaborators / instruments. Note AUP change.
25% of ESnet traffic
340Gbps extension.

## Slide 10: ESnet Strategy (in addition to world-class operations…)
Discovery is unconstrained by geography.
2. Provide information and tools for optimal network use.
vision:
goals:
3. Pioneer architectures, protocols, applications.
1. Improve networking practices globally.

## Slide 11
Network as Infrastructure Instrument
Connectivity is the first step – usability must follow

## Slide 12
80% of ESnet traffic originates or terminates outside the DOE complex.
ESnet’s success is necessary but not sufficient for DOE, because networks share fate. SC invests nearly $1B/year in university research: campus networks matter.

## Slide 13: The Science DMZ in 1 Slide
Consists of four key components, all required:
“Friction free” network path
  Highly capable network devices (wire-speed, deep queues)
  Virtual circuit connectivity option
  Security policy and enforcement specific to science workflows
  Located at or near site perimeter if possible
Dedicated, high-performance Data Transfer Nodes (DTNs)
  Hardware, operating system, libraries all optimized for transfer
  Includes optimized data transfer tools such as Globus Online and GridFTP
Performance measurement/test node
  perfSONAR
Engagement with end users
  Details at http://fasterdata.es.net/science-dmz/
© 2013 Wikipedia
Notes: Single slide summary

## Slide 14: Science DMZ now recognized as a global best practice.
NSF is investing $60M to promote adoption by US universities (among other CI goals). Fourth funding round underway.
>120 universities in the US have deployed this DOE architecture.
In addition: USDA, NIH – with NASA, NOAA investigating.
Australian, Canadian universities following suit.

## Slide 15: What’s next? Evolution of Science DMZ as a regional cyberinfrastructure platform.
Recent announcement of Pacific Research Platform initiative:
first large-scale effort to coordinate and integrate Science DMZs
participation by all major California R&E institutions, CENIC, ESnet
announced March 6: http://cenic.org/news/item/high-performance-big-science-pacific-research-platform-debuts-at-cenic

## Slide 16
By 2025, DOE light sources will be transformed by high-resolution detectors, advanced mathematical analysis techniques, robotics, software automation, programmable networks.
Detectors capable of generating terabit data streams.
Computational tools for analysis, data reduction, feature extraction in situ, using advanced algorithms and specialized hardware.
Increased scientific throughput from robotics and automation software.
Data management and sharing, with federated identity management and flexible access control.
Post-processing: reconstruction, inter-comparison, simulation, visualization.
Integration of experimental and computational facilities in real time, using programmable networks.
Superfacility instances multiply.

## Slide 17
ESnet
New Math
High performance Software
Novel compute/data platforms
Program-mable network
Data mgmt. and sharing
Real-time analysis
Extreme Data Science Facility (XDSF)
MS-DESI
ALS
JGI
APS
LCLS
Other data-producing sources
LHC
Superfacility Vision: : A network of connected facilities, software and expertise to enable new modes of discovery
Notes: DOE should have a facility dedicated to …

## Slide 18: Superfacility Prototype and Use Case : Process of science transformed
Real-time analysis of ‘slot-die’ technique for printing organic photovoltaics, using ALS + NERSC (SPOT Suite for reduction, remeshing, analysis) + OLCF (HipGISAXS running on Titan w/ 8000 GPUs).
1
2
http://www.es.net/news-and-publications/esnet-news/2015/esnet-paves-way-for-hpc-superfacility-real-time-beamline-experiments/
Results presented at March 2015 meeting of American Physical Society by Alex Hexemer.
Additional DOE contributions: GLOBUS (ANL), CAMERA (Berkeley Lab)

## Slide 19: engage@es.net
Jason Zurawski – zurawski@es.net
Science Engagement Engineer, ESnet
Lawrence Berkeley National Laboratory
Future Trends in Nuclear Physics Computing
March 18th 2016