## Slide 1: JLEIC Concept
Speaker: V.S. Morozov (JLab)
on behalf of JLEIC Collaboration

## Slide 2: Electron Ion Collider
Recommendations in NSAC LRP 2015:
Continue existing projects: CEBAF, FRIB, RHIC.
“…a U.S.-led ton-scale neutrinoless double beta decay experiment”
“…a high-energy high-luminosity polarized EIC as the highest priority for new facility construction following the completion of FRIB”
“…small-scale and mid-scale projects and initiatives that enable forefront research at universities and laboratories”
EIC Community White Paper arXiv:1212.1701

## Slide 3: JLEIC Status
JLEIC conceptual design is nearly complete
Key features:
  Modern technology
  High luminosity
  High polarization
  Full-acceptance detection
Current work
  Key R&D
    High-energy electron cooling
    IR magnet prototyping
    Crabbing experiment
    Spin dynamics experiment
    Simulation software development
  Completion of consistent design
  Performance and cost optimization
  Evaluation of engineering challenges
  Completion of a pre-CDR

## Slide 4: JLEIC Collaboration
S. Benson, A. Bogacz, P. Brindza, A. Camsonne, E. Daly, Ya.S. Derbenev, M. Diefenthaler, D. Douglas, R. Ent, Y. Furletova, D. Gaskell, R. Geng, J. Grames, J. Guo, F. Hanna, L. Harwood, T. Hiatt, Y. Huang, A. Hutton, K. Jordan, G. Kalicy, A. Kimber, G. Krafft, R. Li, F. Lin, F. Marhauser, R. McKeown, T. Michalski, V.S. Morozov, P. Nadel-Turonski, E. Nissen, H.K. Park, F. Pilat, M. Poelker, R. Rajput-Ghoshal, R. Rimmer, Y. Roblin, T. Satogata, M. Spata, R. Suleiman, A. Sy, C. Tennant, H. Wang, S. Wang, G.H. Wei, C. Weiss, M. Wiseman, R. Yoshida, H. Zhang, Y. Zhang - JLab, VA
D.P. Barber - DESY, Germany
Y. Cai, Y.M. Nosochkov, M. Sullivan - SLAC, CA
S. Manikonda, B. Mustapha, U. Wienands - Argonne National Laboratory, IL
P.N. Ostroumov, R.C. York - Michigan State University, MI
S. Abeyratne, B. Erdelyi - Northern Illinois University, IL
J. Delayen, H. Huang, C. Hyde, K. Park, S. De Silva, S. Sosa, B. Terzic - Old Dominion University, VA
P. Nadel-Turonski, SUNY, NY
Z. Zhao - Duke University, NC
A.M. Kondratenko, M. Kondratenko - Sci. & Tech. Laboratory Zaryad, Russia
Yu. Filatov - Moscow Institute of Physics and Technology, Russia
J. Gerity, T. Mann, P. McIntyre, N.J. Pogue, A. Sattarov - Texas A&M University, TX
V. Dudnikov, R.P. Johnson - Muons, Inc., IL
I. Pogorelov, G. Bell, J. Cary - Tech-X Corp., CO
D. Bruhwiler - Radiasoft, CO

## Slide 5: JLEIC Layout
3-12 GeV
8-100 GeV
8 GeV
May 17 parameter update:
https://eic.jlab.org/wiki/index.php/Main_Page
SRF Linac &
Electron complex
  CEBAF
  Electron collider ring
Ion complex
  Ion source
  SRF linac (285 MeV/u for protons)
  Booster
  Ion collider ring
Up to two detectors at minimum background locations
2015
2012
arXiv:1209.0757
arXiv:1504.07961
Completed by
October 2018

## Slide 6: Why EIC Should be Built at JLab
Large established user community in the field
CEBAF, the world highest energy SRF linac, as a full energy injector
  Maintains highly-polarized high-current electron beam in the electron collider ring using demonstrated top-up injection technique
Green Field collider complex
  Modern design and technology
  No constraints imposed by existing infrastructure
  Design driven by experimental requirements
    Novel high luminosity concept
    Luminosity optimized around the CM range of physics interest
    Novel figure 8 design for high polarization of any particles including deuterons
    Deeply integrated detector and machine design for full acceptance
  Balance of good performance and low technical risk

## Slide 7: Key Design Concepts
High luminosity: high collision rate of short modest-charge low-emittance bunches
  Small beam size
    Small β*  Short bunch length  Low bunch charge, high repetition rate
    Small emittance  Cooling
  Similar to lepton colliders such as KEK-B with L > 21034 cm-2s-1
High polarization: figure-8 ring design
  Net spin precession zero
  Spin easily controlled by small magnetic fields for any particle species
Full acceptance primary detector including far-forward acceptance
Beam Design
High repetition rate
Low bunch charge
Short bunch length
Small emittance
IR Design
Small β*
Crab crossing
Damping
Synchrotron radiation
Electron cooling

## Slide 8: JLEIC Energy Reach and Luminosity
CM Energy (in each scenario) | Main luminosity limitation
low | space charge
medium | beam-beam
high | synchrotron radiation
Current baseline
Alternative/
upgrade
options

## Slide 9: 12 GeV CEBAF as Injector
Extensive fixed-target science program
  Fixed-target program compatible with concurrent JLEIC operations
JLEIC injector
  Fast fill of collider ring
  Full energy
  ~85% polarization
  Enables top-off
New operation mode but no hardware modifications
Up to 12 GeV
to JLEIC

## Slide 10: Electron Beam
Electron beam
  3 A at up to 7 GeV
  Normalized emittance 54 µm @ 5 GeV
  Synchrotron power density < 10 kW/m
  Total power up to 10 MW

## Slide 11: Electron Polarization
Estimated polarization lifetime
At high energies (> ~5 GeV), constant polarization is maintained by continuous injection of highly polarized (~85%) electron beam from CEBAF
A relatively low average injected beam current of tens-of-nA level can maintain a high equilibrium polarization in the whole energy range
Beam lifetime must be balanced with the beam injection rate and
Energy (GeV) | 3 | 5 | 7 | 9 | 10
Lifetime (hours) | 66 | 8 | 2.2 | 0.9 | 0.3

## Slide 12: Polarization
Figure-8 concept: Spin precession in one arc is exactly cancelled in the other
Spin stabilization by small fields: ~3 Tm vs. < 400 Tm for deuterons at 100 GeV
  Criterion: induced spin rotation >> spin rotation due to orbit errors
3D spin rotator: combination of small rotations about different axes provides any polarization orientation at any point in the collider ring
No effect on the orbit
Polarized deuterons
Frequent adiabatic spin flips
n = 0

## Slide 13: Start-to-End Deuteron Acceleration in Ion Collider Ring
Three deuterons with and accelerated at ~3 T/min in lattice with 100 m rms closed orbit excursion,
Deuteron spin is highly stable in figure-8 rings, which can be used for high precision experiments
Analytic prediction
(Zgoubi simulation)

## Slide 14: Multi-Stage Cooling Scheme
Cooling of JLEIC proton/ion beams for
  Achieving small emittance (~10x reduction)
  Reaching short bunch length ~1 cm (with SRF)
  Suppressing IBS induced emittance degradation
Ring | Functions | Kinetic energy (GeV / MeV) |  |  | Cooler type
 |  | Proton | Lead ion | Electron | 
booster ring | Accumulation of positive ions |  | 0.1 (injection) | 0.054 | DC
collider ring | Maintain emitt. during stacking | 7.9 (injection) | 2 (injection) | 4.3 (proton) 1.1 (lead) | DC
 | Pre-cooling for emitt. reduction | 7.9 (injection) | 7.9 (ramp to) | 4.3 | DC
 | Maintain emitt. during collision | Up to 100 | Up to 40 | Up to 54.5 | ERL
Can’t reduce emittance due to space charge limit
ERL cooler can’t reach energy below 20 MeV
Pre-cooling both protons and lead ions
Pre-cool when energy is low
Cool when emittance is small
(after pre-cool at low energy)

## Slide 15: High-Energy Electron Cooling
Magnetized electron beam for higher cooling efficiency
Cooling electron beam is energy-recovered to minimize power consumption
Circulator ring to relax electron source requirements
  Ultra-fast harmonic kicker to kick electrons in and out of the circulator ring

## Slide 16: ERL-Circulator Cooler Design and R&D
Magnetized source
Beamline
Gun Solenoid
Gun HV Chamber
beamline
Gun HV chamber
Gun solenoid
magnetized beam
Harmonic RF Fast kicker
10 harmonics
5 harmonic prototype
S2E simulation after booster
Long. phase space@200 kV
Design and BD & Future Beam Tests at IOTA

## Slide 17: Detector Region
Integrated detector region design developed satisfying requirements of detection, beam dynamics and geometric match
GEANT4 detector model developed, simulations in progress
Forward hadron spectrometer
low-Q2 electron detection
and Compton polarimeter
p
(top view in GEANT4)
e
ZDC
IP
e
ions
forward e detection
Compton polarimetry
dispersion suppressor/
geometric match
spectrometers
forward ion detection

## Slide 18: Ion Beam Envelope & 99%p Trajectory
Assuming beam momentum of 100 GeV/c, ultimate normalized x/y emittances of 0.35/0.07 m, and ultimate momentum spread of 310-4
The horizontal size includes both betatron and dispersive components
2nd focus
IP

## Slide 19: IR Quadrupole Prototype
Collaborative project by BNL, JLab, and LBNL supported by DoE EIC R&D funds
One superconducting magnet will be built and tested – will be similar to the magnet needed for the EIC
The superconducting coils to be used in the magnet will be coils that were built as part of another program
Design of the magnet will incorporate results from detailed computer models and from tests of similar magnets
Test results - compared with the predictions of the models

## Slide 20: Beam Crabbing
Bob Palmer’s Solution
Low luminosity
Beam dynamics issues
Effective head-on collision restored
Factor of 10 luminosity increase compared to uncorrected case
Beam crossing angle is necessary to avoid parasitic collisions due to short bunch spacing, make space for machine elements, improve detection and reduce detector background

## Slide 21: Crabbing Test at CERN’s SPS
First SPS ion crabbing test completed: crab cavity turned on and bunch tilt observed
ODU, JLab and BNL plan to participate in future tests

## Slide 22: FY 18-19 JLab EIC R&D Projects Supported by DoE
Crab cavity operation in a hadron ring (Lead: ODU, collaborators: JLab, BNL)
Development of innovative high-energy magnetized electron cooling for an EIC (Lead: JLab, collaborators: BNL, FNAL, ODU)
Strong hadron cooling with micro-bunched electron beams (Lead: BNL, collaborators: JLab, SLAC, ANL)
High Gradient Actively Shielded Quadrupole (Lead: BNL, collaborators: JLab, LBNL)
Validation of EIC IR magnet parameters and requirements using existing magnet results (Lead: JLAB, collaborators: SLAC, LBNL)
Development & test of simulation tools for EIC beam-beam Interaction (Lead: BNL, collaborators: JLab, MSU, LBNL)
Experimental verification of spin transparency mode in an EIC (Lead: JLab, collaborator: BNL)
High Bandwidth Beam Feedback Systems for a High Luminosity EIC (Lead: ANL, collaborator: JLab)

## Slide 23: pCDR Planning and Status
Keep in mind pCDR milestones:
  Early section drafts: June 1 2018
  Early draft full document: June 18 2018 (JLab Users Group)
  Solid draft full document: July 30 2018 (EIC Users Group)
  Deliver full document: Sep 28 2018 (End of FY18)

## Slide 24: Backup

## Slide 25: JLEIC Parameters (3T option)
CM energy | GeV | 21.9 (low) |  | 44.7 (medium) |  | 63.3 (high) | 
 |  | p | e | p | e | p | e
Beam energy | GeV | 40 | 3 | 100 | 5 | 100 | 10
Collision frequency | MHz | 476 |  | 476 |  | 476/4=119 | 
Particles per bunch | 1010 | 0.98 | 3.7 | 0.98 | 3.7 | 3.9 | 3.7
Beam current | A | 0.75 | 2.8 | 0.75 | 2.8 | 0.75 | 0.71
Polarization | % | 80% | 80% | 80% | 80% | 80% | 75%
Bunch length, RMS | cm | 3 | 1 | 1 | 1 | 2.2 | 1
Norm. emittance, hor / ver | μm | 0.3/0.3 | 24/24 | 0.5/0.1 | 54/10.8 | 0.9/0.18 | 432/86.4
Horizontal & vertical β* | cm | 8/8 | 13.5/13.5 | 6/1.2 | 5.1/1.0 | 10.5/2.1 | 4/0.8
Ver. beam-beam parameter |  | 0.015 | 0.092 | 0.015 | 0.068 | 0.008 | 0.034
Laslett tune-shift |  | 0.06 | 7x10-4 | 0.055 | 6x10-4 | 0.056 | 7x10-5
Detector space, up/down | m | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3 | 3.6/7 | 3.2/3
Hourglass(HG) reduction |  | 1 |  | 0.87 |  | 0.75 | 
Luminosity/IP, w/HG, 1033 | cm-2s-1 | 2.5 |  | 21.4 |  | 5.9 |