## Slide 1
Physics Requirements
Sensitivity to Manufacturing Imperfections
Strategy
  where to map field
  measure deviation from ideal model
  fit to error tables
Conceptual Design
Project Plan
  prototyping, data-taking plans, analysis plans
CLAS12 Torus Magnetic Field Mapping
Measurement Team
Physicist: Mac Mestayer
Hall B Engineers: Renuka Ghoshal, Probir Ghoshal, Ruben Fair
Accelerator: Ken Baggett, Joe Meyers
Shift Personnel: collaboration
Notes: Outline: see slide 10 for quick answers to each point

## Slide 2
CLAS12 Torus Magnetic Field Mapping
Physics Requirement
Best dp/p resolution is from particle trajectories near the beam-line (highest B-field)  low-angle elastic scattering
Here is the trajectory of an elastically scattered electron from 11 GeV beam
(p = 10.1 GeV/c, q = 7o)
For this track, dp/p ~ 0.3%
 need to know to ~ 0.1%

## Slide 3: Strategy for Mapping and Adjusting the CLAS12 Torus Magnetic Field
Two types of distortions:
expected from design, (e.g. shrinkage at low temperature ) and
those due to small manufacturing differences (like one coil being shifted in z, or one coil not being wound as tight as another, etc.).
Strategy to map and adjust the magnetic field:
include any average distortions from design as part of the nominal field calculation
calculate the error B-field*, i.e.(Bdistorted- Bnominal), for various anticipated distortions due to manufacturing tolerances
after mapping, fit (Bmeasured - Bnominal) to a sum of these "error B-fields" scaled by adjustable coefficients

## Slide 4
% Change in B-field:
plotted vs. radius
coil stack too large by 2mm
coil moved down, centered, up
2 mm increase in stack size can cause field distortions of up to a few parts per thousand
large radius surface of inner coil is most critical dimension
Effect of Distortion in Coil-Winding
Notes: Here is a plot of the fractional deviation of the B-field from ideal (measured at the mid-plane between coils, for
radii between 0.5 and 2 m) for a coil that was made with a stack height 2mm too large. Upper left: closest to
beam edge aligned, upper right: centered, below left: coil aligned on outer edge. Main point: 1 -2mm imperfections
create problems which are barely at the noticeable level.

## Slide 5: Effect of Change in Coil Stack Height of 1 mm
Chart: dB variation along Z at 15deg at R=0.4m
| 2 | 2.2000000000000002 | 2.4 | 2.6 | 2.8 | 3 | 3.2 | 3.4 | 3.6 | 3.8 | 4 | 4.2 | 4.4000000000000004 | 4.5999999999999996 | 4.8 | 5
dBx (Gauss) | -0.12746 | -0.28729 | -0.6861 | -1.7045 | 8.346 | 5.2194 | -3.5308 | -8.1854 | -12.3018 | -13.4468 | -14.2409 | -15.7323 | -2.8387 | 23.0125 | -6.0542 | -3.4725
dBy (Gauss) | -0.037987 | -0.08016 | -0.21806 | -0.98435 | -5.2936 | 13.271 | 3.7273 | 6.3598 | 10.2065 | 10.6839 | 10.7282 | 10.9199 | 9.4987 | -9.4745 | -4.9633 | -0.77517
dBz (Gauss) | -0.065577 | -0.14289 | -0.41563 | -1.9702 | -9.9042 | 6.6013 | -3.9506 | -1.0642 | -0.23139 | -0.12257 | -0.31535 | -2.9833 | -15.1089 | 2.9836 | 8.0894 | 1.5863
~ 18 Gauss change
in field; ~ 0.1 %

## Slide 6
Need to know
radius to ~ 0.1mm

## Slide 7: Fitting the Measurements
Number of measurements
  6 (sectors) x 4 (x-y posn’s) x 3 (dim.) x 50 (z posn’s) = 3600
Method
  fit measured deviation from ideal to adjustable parameters which scale tables of calculated deviations from ideal due to ‘unit distortions’
Number of parameters
  6 (coils) x [ 2 (movements) + 1 (expansion) ] x 3 (dim.) = 36
6 total; is 2 enough?

## Slide 8: Definition of c2
c2
=
sum over measurement points and dimensions
table of measurements minus ‘ideals’
pre-calculated table of ideal field plus fields due to
‘unit distortions’
adjustable parameters

## Slide 9: How Are We Going to Map?
Digital Voltage
Meter
Hall Probes in Sensor Block
Three 1-dimensional probes
measure ~ every 5cm in Z
Measurement Tubes
non-magnetic
~ 2” diameter Carbon
linear stage

## Slide 10
Magnet Mapping Sensor Head Mechanical Sketch

## Slide 11: Torus Mapper Prototype: Build
Shim and adjust test magnet
  field strength of ~2 Tesla
  enlarge gap to accommodate one measurement tube and assembly
  produce gradient of ~2% per cm
Procure and build prototype
  - sensor
    cylindrical sensor head containing three 1-dimensional Hall probes
    connection to translation rod
    electrical connections
  - tube
    tube assembly
    attachment and survey points
  - translation system
  - analysis and display software
  - control system: motion, data-taking runs, interlocks,

## Slide 12: Torus Mapper Prototype: Test
Test operation of prototype
  Do all systems work?
    placement and survey
    rotating and moving of sensor
    signal readout under various conditions; noise measurement
    quick ‘real-time’ analysis of results
  Do procedures make sense? How long does a scan take?
Verify reproducibility to better than 0.1%
  many scans, no changes
  changing step size
  changing position within magnet; removing, replacing
  changing orientation with respect to gravity
Calibration of Hall probes

## Slide 13: Tube Holder ?
Move 1 Sensor or Fixture Holds Several ?
my vote Move 1 Sensor via Links
  Pro: mapping location flexible; single probe calibration
  Con: need to survey all locations within one sector
  Issues: where to locate link ends ? beam axis ?
  Move to exact position ?
     more complicated hardware, survey procedure
  Move to approx. position and survey ?
    more complicated software

## Slide 14: Torus Mapping Timelines
 | Sep |  | Oct |  | Nov |  | Dec |  | Jan |  | Feb |  | Mar |  | Apr |  | May |  | Jun |  | Jul |  | Aug |  | Sep | 
Sensor Conceptual Design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Prototype Sensor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Fixture Design |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mapper Built |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Location, Procedure Verified |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Torus Ready for Installation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mapper Installed |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Torus Commissioned |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Mapping Done |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 15
Physics Requirements : measure field to 0.1% accuracy at a radius known to 0.1mm
Sensitivity to Manufacturing Imperfections ~ 1mm
Strategy
  where to map field : 4 locations each sector, ~25 – 50 pts in z
  measure actual, calculate deviation from ideal model
  fit to error tables : with adjustable strength
Conceptual Design
  moving sensor head with 3 Hall probes
Project Plan
  timeline: prototype in fall 2015, build in spring, map in June
Summary
Notes: brief answers to the various points