## Slide 1: CLAS12 Beamline Configurations
R. DeVita M. Ungaro

## Slide 2: Starting from…
W/O FT Configuration
~0.8% occupancy in R3
With FT Configuration
~3% occupancy in R1
Shield starts at z ~ 420mm
Shield starts at z ~ 750mm
Notes: This was the starting point after 2-3 years of studying background and adding shields. General description of left and right pics.
The shield is shaped as a truncated cone, pointing to to the CLAS12 center
The shield is made of a single material, i.e. tungsten
The shape and positioning of the shield was based on accurate studies of the beam sausage, details in the next two slides.
W: alloy of W and Fe

## Slide 3: Beam profile studies
32 disks used to sample particles fluxes from z=40 cm to z=102 cm every 2 cm, covering up to 35 deg.
New beam profile studies for different configurations between target and shield:
Air
Vacuum
He4
FMT included
85%, 75% solenoid field

## Slide 4: Beam profile (Air)
Profile at Z=750mm (entrance of Moller Cone in FT configuration)
All particles
Electrons
Moller electrons
Moller electrons with E>200MeV
Photons
Other
Photons and neutrons spread at all angles
Electrons “contained” by solenoid field
Beam “radius” defined from edge of moller electron distribution

## Slide 5: Nov 2015 to Feb 2016
Bob Miller
Mike Zarecky
Latifa Elouadrhiri
Volke Burkert
Glenn Young
Stepan Stepania
Raffaella DeVita
Maurizio Ungaro
Francois Xavier
David Riser
Costs
Support
Practicality: switching configuration
Notes: A committee was formed

## Slide 6: Starting from…
“physicist design”
Very hard to support weight
Finalize torus mount so it’s same for both configurations
Notes: This was the starting point after 2-3 years of studying background and adding shields. General description of left and right pics.
The shield is shaped as a truncated cone, pointing to to the CLAS12 center
The shield is made of a single material, i.e. tungsten
The shape and positioning of the shield was based on accurate studies of the beam sausage, details in the next two slides.

## Slide 7: Simulating 1035 luminosity
1 event is 250 ns long, 124,000 e- on LH2 target, bunched every 4 ns
Speeds up:
Fixed and simplified geometry, overlaps
Luminosity mechanism improved
Simplified Range Kutta
Production Cut
1 event: ~110 seconds on farm, or 0.8 msec / electron on target
Statistics:
10K events = 1.2 billion e- on target / configuration
Total: ~ 0.1 trillion e- on target
Notes: A committee was formed

## Slide 8: Torus Mount, Torus Bore
Tungsten Shield around Al beampipe inside torus, 2cm, 12 cm OD
Torus Warm Bore
Torus Warm Bore Shield
Torus Cold Hub
Also: torus vacuum jacket, plates, coils box and coils all re-designed

## Slide 9: Four “realistic” configurations
No FT shield. Still hard to support weight.
FT configuration.
All same mount to torus
FT non operational, used as shield
No FT, but same shield as FT

## Slide 10: FT Cone. No FT. Lead in place of FT.
R=120 at z=1444mm: 4.75o
Torus Start: z=2753mm
Mount Start: z=2270mm
SST Support inside tube and cone
Notes: Top: simulation implementation. Bottom: engineering design

## Slide 11: FT not operational, as shielding.
Torus Start: z=2753.8mm
Mount Start: z=2269.6mm
R=120 at z=1444mm: 4.75o

## Slide 12: FT not operational, as shielding.
R3 Background Source
R1 Background Source

## Slide 13: Four “realistic” configurations
No FT shield. Still hard to support weight.
FT configuration.
All same mount to torus
FT non operational, used as shield
No FT, but same shield as FT
R1: 0.7%
R3: 0.6%
R1: 1.75%
R3: 1.0%
R1: 1.0%
R3: 0.66%
R1: 1.0%
R3: 0.6%
Conclusions: can use same shield, just move it!
Notes: Very promising results on using same shield.

## Slide 14: January 2016: Modifications
Torus was 25cm too long. Coils now in correct position. Hub Plates. All Tungsten is now RED.
Baseline Reference

## Slide 15: January 2016: Modifications
Tracker removed. More Shielding. Additional Piece to FT Cone.
With FT as shielding

## Slide 16: January 2016: Modifications
Beampipe 0.125” thick (3.175mm), was 2mm. OR = 30. OR 40 in torus. OR 66 downstream
With FT as shielding

## Slide 17: January 2016: Modifications
D. Riser: DC Mount Plates, Overlaps fixes.
With FT as shielding

## Slide 18: January 2016: Modifications
Mount thicker. Less than anticipated shielding inside, but outside shielding.
With FT as shielding

## Slide 19: January 2016: Engineer Analyses
Calculations
FEA of assembly with tungsten tube
FEA of assembly with stainless steel tube
Bolt analysis
Weld Analysis
Point Masses:
Lead shield 267 lbs
Forward Tagger 625 lbs
Inner mount shield 60 lbs (ID 60 mm, OD 88 mm, Length 480 mm)
Outer mount shield 194 lbs (ID 191 mm, OD 231 mm, Length 380 mm)
Load Cases
Gravity
Gravity, and acceleration of 0.1G in X, Y, and Z (this analysis will be added when the final details of the assembly are completed)

## Slide 20: New Baseline
Before
After

## Slide 21
Before
After
New Baseline
Mount Start: 2270
Torus Start: 2750

## Slide 22: Reality, No FT
Before
After

## Slide 23
Before
After
Reality, No FT
Mount Start: 2270
Torus Start: 2750
FT Cone END: 1444

## Slide 24: Reality, FT is shield
Before
After

## Slide 25
Before
After
Reality, FT is shield
Mount Start: 2270
Torus Start: 2750
FT Cone END: 1444

## Slide 26: Reality, With FT
Before
After

## Slide 27
Before
After
Reality, With FT
Mount Start: 2270
Torus Start: 2750
FT Cone END: 1760

## Slide 28: Reality, FT is shield
Full Solenoid
75% Solenoid
50% Solenoid

## Slide 29: FT: field strength effect
Spot size increases significantly at lower field
Moller cone entrance radius could be smaller than beam spot
Solution if full field would not be available ➙ move cone upstream
  No effect on CLAS12 acceptance
  Reduction of FT angular coverage
  Can be implemented via modular design for in-situ optimization depending on solenoid field
Beam spot “angle” defined as:
Angle = tan-1(R/Z)
Present FT design (realityWithFT)

## Slide 30: Material between target and shield
Vacuum
Air
Air+FMT
Helium
Lower dc occupancy for vacuum or helium
Small reduction with FMT due to shielding of low energy particles

## Slide 31: Physics Processes

## Slide 32: Physics Processes

## Slide 33: Physics Processes

## Slide 34: Physics Processes

## Slide 35: Physics Processes

## Slide 36: Physics Processes
MeV

## Slide 37: Summary: two configurations
Same FT shield can be used when FT is not in used.
Removal of FT tracker has minimal schedule impact.
Hot spot in Torus Mount can be shiel
Helium between target and shield improves background by:
~ 10% if FT is used
~ 50% if FT is used – at which point the occupancy is < 1% in R1
Narrowed it down to two configurations