## Slide 1: JLEIC Hadron Bunch Splitting Simulations
Todd Satogata and Randika Gamage
IPAC’16 Paper
http://accelconf.web.cern.ch/AccelConf/ipac2016/papers/wepmw013.pdf

## Slide 2: The Earlier Problem
JLEIC (MEIC) Arxiv paper: 1504.07961v1.pdf
Specified hadron bunch splitting from h=9 (injection and acceleration RF) to h=6832 (storage and collision RF)
Unprecedented splitting, hadron bunch length/RF freq
  State of the art: 1->12 (CERN PS for LHC)

## Slide 3: The Updated Problem
Jiquan provided an update to a bunch formation scheme in slides on Jun 24 2016 (with an update at this meeting)
h=1792
h=56, 112, 224, 448, 896
h=3584
h=56, Circumference=40.28m*56=2255.75m
Quasi-coasting beam instabilities?

## Slide 4: Hadron Collider Comparison

## Slide 5: Debunch/Rebunch
The old conventional method for changing the longitudinal structure of the beam is to debunch by cancelling the voltage at the initial frequency, to drift without longitudinal focusing, and to rebunch withanother RF frequency. To minimize emittance blow-up, voltage variations have to be iso-adiabatic over a large dynamic range. Although widely used, this technique presents a number of drawbacks:
  RF voltages must be controlled down to small amplitudes in the presence of beam loading,
  While drifting, the beam is left uncontrolled,
  The full circumference is filled with particles,
  The continuous beam has a very small Δp/p which makes it prone to microwave instability.
Randy is simulating debunch/rebunch at present, including realistic impedances as measured at RHIC
Can be applied to barrier bucket scheme as well: small Δp/p?
(R. Garoby)

## Slide 6: 9:18 Debunch/Rebunch (no impedance)

## Slide 7: Debunch/Rebunch (no impedance)

## Slide 8: Bunch Splitting
CERN PS splits 6:18 (3x) then 18:36 (2x) then 36:72 (2x)
Fig 7.1, LHC design report
20 ns/div.
Figs 7.3-4, LHC design report

## Slide 9: Adiabatic Bunch Splitting
Have put parameter set into ESME
  Fermilab longitudinal dynamics (only) code
    faster, longitudinally oriented compared to many other codes
  Have running on cluster (e.g. jlabl4) for GA optimizations
  Optimize split times, voltages vs longitudinal emittance growth
  Have source code, support from Francois Ostiguy at Fermilab
Good 1:2 split
Bad 1:2 split

## Slide 10: Single Split Optimization
Bunch splitting for JLEIC requires several splits
  Each splitting must be reasonably well-optimized
  Even small (few percent) longitudinal emittance growth per split becomes intolerable
Conditions for emittance growth
  Initial longitudinal emittance very small
  Bunch splitting too fast (non-adiabatic)
Parameterize transverse emittance growth in 2:1 split
  Use scaled parameters for universality
  vs initial emittance/bucket size
  vs splitting time/initial synchrotron period
  Used JLEIC first split (h=9 to h=18) parameters
  Plot relative emittance growth vs two “vs” parameters

## Slide 11: Parameter Scan Results (1)
Region of large emittance growth
  Small split time and/or small initial emittance
  Relative emittance growth: well over 100%

## Slide 12: Parameter Scan Results (2)
Region of modest emittance growth
  Requires split time to be 100+ synchrotron periods
  But given that, almost immune to initial bunch size

## Slide 13: Bunch Split Scaling
Assume bucket area scales as the split
  Initial area is evenly divided into split buckets
  Implies that RF voltage doubles with every split
    E.g. VRF,h=18 = 2VRF,h=9 for first split
  Synchrotron period scaling is then that synchrotron period halves with every successive split
    Ts,h=9 = 2 Ts,h=18
    Can make splits faster at higher harmonics

## Slide 14: 29 Split Simulation: Initial Conditions

## Slide 15: 29 Split Simulation: Halfway Through

## Slide 16: 29 Split Simulation: After All Splits

## Slide 17: Esme Microwave Instability Simulation
From Chris Beltran’s PhD Thesis, 2004
Impedance-driven longitudinal instability in Los Alamos PSR