## Slide 1: Update on GHOST Code Development
Balša Terzić
Department of Physics, Old Dominion University
Center for Accelerator Studies (CAS), Old Dominion University
JLEIC Collaboration Meeting, Jefferson Lab, October 5, 2016

## Slide 2: Interdisciplinary Collaboration
Jefferson Lab (CASA) Collaborators:
Vasiliy Morozov, He Zhang, Fanglei Lin, Yves Roblin, Todd Satogata
Old Dominion University (Center for Accelerator Science):
  Professors: Physics: Balša Terzić, Alexander Godunov Computer Science: Mohammad Zubair, Desh Ranjan
  Students: Computer Science: Kamesh Arumugam, Ravi Majeti
  Physics: Chris Cotnoir, Mark Stefani

## Slide 3: Outline
Motivation and Challenges
    Importance of beam synchronization
    Computational requirements and challenges
  GHOST Code Development: Status Update
    Review what we reported last time
    Toward new results
      Implementation of beam collisions on GPUs
      “Gear change” on the horizon
Checklist and Timetable

## Slide 4: Motivation: Implication of “Gear Change”
Synchronization – highly desirable
  Smaller magnet movement
  Smaller RF adjustment
Detection and polarimetry – highly desirable
  Cancellation of systematic effects associated with bunch charge and polarization variation – great reduction of systematic errors, sometimes more important than statistics
  Simplified electron polarimetry – only need average polarization, much easier than bunch-by-bunch measurement
Dynamics – question
  Possibility of an instability – needs to be studied (Hirata & Keil 1990; Hao et al. 2014)
Fast beam
Slow beam

## Slide 5: Computational Requirements
Perspective: At the current layout of the JLEIC 1 hour of machine operation time ≈ 400 million turns
Requirements for long-term beam-beam simulations of JLEIC
    High-order symplectic particle tracking
    Speed
    Beam-beam collision
    “Gear change”
We employ approximations which speed computations up:
  One-turn maps
  Approximate beam-beam collision (Bassetti-Erskine)

## Slide 6: GHOST: Outline
GHOST: Gpu-accelerated High-Order Symplectic Tracking
GHOST resolves computational bottlenecks by
  Uses one-turn maps for particle tracking
  Employing Bassetti-Erskine approximation for collisions
  Implementing the code on a massively-parallel GPU platform
GPU implementation yields best returns when:
  The same instruction for multiple data (particle tracking)
  No communication (particle tracking; parallel collision)
Two main parts:
    Particle tracking
    Beam collisions

## Slide 7: Reported at the Last Meeting
Long-term simulation require symplectic tracking
GHOST implements symplectic tracking just like COSY
  Demonstrated equivalency of results
GHOST tracking results match those with elegant
  Elegant is element-by-element, GHOST one-turn map
GPU implementation of GHOST tracking speeds execution up
  Execution on 1 GPU over 1 CPU is over 280 times faster
Collisions in GHOST done on a CPU only
  Hourglass effect reproduced
  Benchmarked with BeamBeam3D – excellent agreement
Tracking: Finished
Collisions: Started

## Slide 8: GHOST: Beam Collisions
Bassetti-Erskine Approximation
  Beams treated as 2D transverse Gaussian slices (Good approximation for the JLEIC)
  Poisson equation reduces to a complex error function
  Finite length of beams simulated by using multiple slices
We generalized a “weak-strong” formalism of Bassetti-Erskine
  Include “strong-strong” collisions (each beam evolves)
  Include various beam shapes (original only flat beams)

## Slide 9: GHOST Benchmarking: Collisions
Code calibration and benchmarking
  Convergence with increasing number of slices M
  Comparison to BeamBeam3D (Qiang, Ryne & Furman 2002)
GHOST, 1 cm bunch 40k particles
Excellent agreement
with BeamBeam3D
BeamBeam3D & GHOST, 10 cm bunch 40k particles
Finite bunch length
accurately represented

## Slide 10: GHOST Benchmarking: Hourglass Effect
When the bunch length σz ≈ β*at the IP, it experiences a
geometric reduction in luminosity – the hourglass effect (Furman 1991)
GHOST, 128k particles, 10 slices
Good agreement with theory

## Slide 11: “Gear Change” with GHOST: Approach
“Gear change” provides beam synchronization for JLEIC
  Non-pair-wise collisions of beams with different number of bunches (N1, N2) in each collider ring (for JLEIC N1 = N2+1 ≈ 3420)
  If N1 and N2 are mutually prime, all combinations of bunches collide
The load can be alleviated by implementation on GPUs
  The information for all bunches is stored: large memory load!
Approach
  Implement single-bunch collision right and fast
  Collide multiple bunches on a predetermined schedule
    Nbunch different pairs of collisions on each turn
Fast beam
Slow beam

## Slide 12: “Gear Change” with GHOST: Toward Results
Gaining confidence in the results:
  Do the single collision right. Compare to BeamBeam3D.
  Reproduce the hourglass effect.
  Collide multiple pairs of bunches at different turns.
  Reasonableness check: 1-1 the same as 10-10?
  Conduct convergence studies.
We will share first results only upon completing all five steps
Technical implementation FINISHED
Validation and benchmarking
UNDERWAY

## Slide 13: “Gear Change” with GHOST: Preliminaries
How GHOST Scales with Bunches and Particles on 1 GPU
Chart: 10K Particles, 3 Slices
| 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0
 | 9.3342 | 16.5165 | 24.0708 | 31.4988 | 39.3198 | 45.4193 | 53.7084 | 61.6273 | 69.554 | 77.1065
Chart: 3 Slices
| 10k | 20k | 30k | 40k | 50k | 60k | 70k | 80k | 90k | 100k
5 Bunches | 31.565 | 37.5628 | 43.8152 | 49.3366 | 54.2698 | 59.108 | 64.7054 | 69.575 | 74.373 | 79.735
8 Bunches | 53.7546 | 64.1897 | 74.7936 | 84.9266 | 92.9485 | 101.0824 | 111.2861 | 119.0318 | 127.1612 | 136.6825
11 Bunches | 77.4823 | 90.9618 | 105.8755 | 119.3982 | 131.9664 | 143.5055 | 156.6955 | 168.5227 | 180.3436 | 192.9964
Linear with the
number of bunches
Linear with the
number of particles
per bunch

## Slide 14: GHOST: Checklist and Timetable
Stage 1: Particle tracking (Year 1: COMPLETED)
  High-order, symplectic tracking optimized on GPUs
  Benchmarked against COSY: Exact match
  400 million turn tracking-only simulation completed
  Submitted for publication (NIM A: waiting since June!)
Stage 2: Beam collisions (Year 1: COMPLETED or UNDERWAY)
  Single-bunch collision implemented on GPUs
  Multiple-bunch collision implemented on a single GPU (arbitrary Nbunch)
  Multiple-bunch validation, checking, benchmarking and optimization
  Multiple-bunch collision implemented on a multiple GPUs
Stage 3: Other effects to be implemented (Year 2 & Beyond)
  Systematic simulations of JLEIC
  Other collision methods: fast multipole
  Space charge, synchrotron radiation, IBS






☐
☐

## Slide 15
Backup Slides

## Slide 16: Last Time: Symplectic Tracking Needed
Symplectic tracking is essential for long-term simulations
Sympletic Tracking
500 000 iterations, 3rd order map
x
Energy not conserved
Particle will soon be lost
Energy conserved
Non-Sympletic Tracking 500 000 iterations, 3rd order map
x
px
px

## Slide 17: Speedup
 |  |  |  | 6Slices | 1Turn |  |  | 
Npart | CPU |  |  | GPU |  |  | Speedup CPU | 
 | Tracking | Collision |  | Tracking | Collision |  |  | 
1000 | 0.644896 | 13.2116 |  | 0.644768 | 15.4794 |  | 0.85 | 
10000 | 1.02157 | 129.49 |  | 1.04451 | 17.9388 |  | 7.22 | 
100000 | 5.86016 | 1287.17 |  | 5.91194 | 29.8827 |  | 43 | 
1000000 | 54.5349 | 12851 |  | 54.8268 | 147.746 |  | 86 | 
 |  |  |  | 10k Particles |  | 6Slices |  | 
Nturn | CPU |  |  | GPU |  |  | Speedup CPU | 
 | Tracking | Collision |  | Tracking | Collision |  |  | 
1 | 1.04202 | 129.479 |  | 1.03523 | 17.823 |  | 7.26 | 
10 | 0.953088 | 131.204 |  | 0.96128 | 17.7718 |  | 7.38 | 
100 | 0.965376 | 143.975 |  | 0.961472 | 17.4446 |  | 8.25 | 
1000 | 0.951872 | 119.376 |  | 0.989312 | 12.4215 |  | 9.61 | 
 |  |  |  | 1Million Patricles |  | 1Turn |  | 
Nslices | CPU |  |  | GPU |  |  | Speedup CPU | 
 | Tracking | Collision |  | Tracking | Collision |  |  | 
1 | 54.473 | 2235.67 |  | 54.8347 | 30.738 |  | 72 | 
2 | 54.4848 | 4396.9 |  | 54.7464 | 54.4933 |  | 81 | 
3 | 54.4546 | 6480.04 |  | 54.7209 | 75.2644 |  | 86 | 
4 | 54.4835 | 8612.99 |  | 54.8068 | 99.6275 |  | 86 | 
5 | 54.5129 | 10708.2 |  | 54.7883 | 125.001 |  | 86 | 
6 | 54.4469 | 12843.6 |  | 54.7732 | 147.913 |  | 87 | 

## Slide 18: Last Time: High-Order Symplectic Maps
Higher-order symplecticity reveals more about dynamics
2nd order symplectic
4th order symplectic
3rd order symplectic
5th order symplectic
5000 turns

## Slide 19: Last Time: Symplectic Tracking With GHOST
Symplectic tracking in GHOST is the same as in COSY Infinity (Makino & Berz 1999)
Start with a one-turn map
Symplecticity criterion enforced at each turn
Involves solving an implicit set of non-linear equations
  Introduces a significant computational overhead
Initial coordinates
Final coordinates

## Slide 20: Last Time: Symplectic Tracking With GHOST
Symplectic tracking in GHOST is the same as in COSY Infinity (Makino & Berz 1999)
Non-Sympletic Tracking 3rd order map
COSY GHOST 100,000 turns
Sympletic Tracking 3rd order map
COSY GHOST 100,000 turns
Perfect agreement!

## Slide 21: Last Time: GHOST Symplectic Tracking Validation
Dynamic aperture comparison to Elegant (Borland 2000)
400 million turn simulation (truly long-term)
GHOST Elegant 1,000 turns
Sympletic Tracking 4th order map
Excellent agreement!

## Slide 22: GHOST: GPU Implementation
100k particles, varying # of GPUs
400 million turns in an JLEIC ring for a bunch with 100k particles:
< 7 hr non-symplectic, ~ 4.5 days for symplectic tracking
1 GPU, varying # of particles
GHOST: 3rd order tracking
Speedup on 1 GPU over 1 CPU over 280 times
With each new GPU architecture, performance improves

## Slide 23: GHOST GPU Implementation
GHOST Tracking on 1 GPU

## Slide 24: JLEIC Design Parameters Used

## Slide 25: “Gear Change” with GHOST
“Gear change” provides beam synchronization for JLEIC
  Non-pair-wise collisions of beams with different number of bunches (N1, N2) in each collider ring (for JLEIC N2 = N1-1 ~ 3420)
    Simplifies detection and polarimetry
    Beam-beam collisions precess
    If N1 and N2 are incommensurate, all combinations of bunches collide
    Can create linear and non-linear instabilities? (Hirata & Keil 1990; Hao et al. 2014)
The load can be alleviated by implementation on GPUs
  The information for all bunches is stored: huge memory load!
Approach
  Implement single-bunch collision right and fast
  Collide multiple bunches on a predetermined schedule
    Nbunch different pairs of collisions on each turn