## Slide 1: IR Design Considerations and Machine Detector Interface for Electron Ion Colliders
Brett Parker
April 11, 2019
8th Workshop of the APS Topical Group on Hadronic Physics from Wednesday, 10 April to Friday, 12 April 2019, Denver, Colorado, USA

## Slide 2: EIC Machine Detector Interface (MDI) Introduction
Experimental Goals
Accelerator Operations
IR Magnet Performance
*This presentation ruthlessly borrows slides from other presentations... please wait for a list of sources when the end credits roll by.
*

## Slide 3: What is needed to address EIC Physics?
polarized electron and hadron (p,d,He-3) beams:
access to spin structure of nucleons and nuclei
Spin vehicle to access the spatial and momentum structure of the nucleon in 3d
Full specification of initial and final states to probe q-g structure of NN and NNN interaction in light nuclei
nuclear beams: D to Pb
accessing the highest gluon densities  saturation
quark and gluon interact with a nuclear medium
high luminosity 1033-34 cm-2s-1:
mapping the spatial and momentum structure of nucleons and nuclei in 3d
access to rare probes, i.e. Ws
large kinematic coverage:
access to x and Q2 over a wide range
 center-of-mass energy √s: 20 – 140 GeV

## Slide 4: Current EIC General Purpose Detector Concepts
Jefferson lab concept: JLEIC
sPHENIX → EIC
Argonne concept: TOPSiDE
Brookhaven concept: BEAST

## Slide 5
Ideal is to measure everything, everywhere. ~100% acceptance for the whole event!
Ion beamline
Electron beamline
Central Detector/Solenoid
Dipole
Dipole
Forward (Ion) Detector
Scattered Electron
Particles Associated
with Initial Ion
Particles Associated with struck parton
What does an idealized EIC detector have?

## Slide 6: EIC IR Design Optimization Logic
All OK
Forward Charged Acceptance
Forward Neutral Acceptance
Rear Acceptance (Polarization & Luminosity Measurements)
Detector / IR Magnet Overlap
Coil Stress Limit
Beam Pipe Design (Lose Aperture)
Field Strength
Coil End Fields (e-beam)
Experimental Goals
Accelerator Operations
IR Magnet Performance
Magnet Strength (Peak Beta)
Field Leakage (e-Beam Synrad)
Field Quality (Harmonic errors, Local Correction Coils)
Magnet Apertures (e-beam & hadron injection)
The IR designer’s challenge is to prove that the valid solution space is not of measure zero.

## Slide 7: EICs are unique colliders.
EIC
LHC /RHIC
collide different beam species: ep & eA
consequences for beam backgrounds
  hadron beam backgrounds,
  i.e. beam gas events
   synchrotron radiation
asymmetric beam energies
boosted kinematics
  high activity at high |h|
High repetition rate
JLEIC: 2.1ns eRHIC 8.7ns between bunches
crossing angle
eRHIC 25mrad JLEIC: 50mrad
wide range in center of mass energies
factor 7
both beams are polarized
 stat uncertainty: ~ 1/(P1P2 (L dt )1/2)
collide the same beam species: pp, pA, AA
 beam backgrounds
  hadron beam backgrounds,
  i.e. beam gas events, high pile up
symmetric beam energies
kinematics is not boosted
  most activity at midrapidity
moderate repetition rate
25 ns between bunches
no crossing angle yet
limited range in center of mass energies
LHC: factor 2
RHIC: factor 26 in AA and 8 in pp
no beam polarization
 stat uncertainty: ~1/(L dt )1/2
Differences impact detector acceptance and possible detector technologies

## Slide 8: IR Design Overview and Conventions
(Outgoing Hadrons)
(Incoming Electrons)
(Incoming Hadrons)
(Outgoing Electrons)
eRHIC Example
Crossing Angle?

## Slide 9: For our EIC, why use a crossing angle?
LHeC Example
Colliding Protons
Electrons
Non-colliding Protons
Synrad
We learn from HERA-II experience that synrad driven background needs careful study.
Both dipole and solenoid fields are here
Forward Side
Rear Side
Does not have RICH
LHeC

## Slide 10: For our EIC, why use a crossing angle?
9.0m
hadrons
electrons
hadronic calorimeters
TPC
e/m calorimeters
silicon trackers
GEM trackers
RICH detectors
3T solenoid coils
BNL concept: BEAST
The HERA and LHeC concepts use separation dipoles to get the beams apart...
and dipoles generate
synrad which can lead to
backgrounds to avoid.
But a crossing angle
geometry needs Crab
Cavities so not to lose
too much luminosity...
The answer is PID.

## Slide 11
EIC PID
needs
are more demanding
then your
normal
collider detector
EIC
needs absolute
particle numbers at
high purity and low
contamination
E
For our EIC, why use a crossing angle?

## Slide 12: For our EIC, why use a crossing angle?
9.0m
hadrons
electrons
hadronic calorimeters
TPC
e/m calorimeters
silicon trackers
GEM trackers
RICH detectors
3T solenoid coils
BNL concept: BEAST
Placing small radius dipoles inside the detector blocks acceptance.
So integrate dipole with solenoid, but then cannot use a RICH!
“Projective” field for a RICH not compatible with a large diameter dipole.
RICH
No dipoles here!
Dipole here?
Dipole here?
JLab concept: JLEIC
RICH
For RICH want tracks aligned with magnetic field

## Slide 13: JLEIC IR Design Layout Schematic
Roman Pots
Forward Side
Rear Side
Forward Side
e-Tagger
Lumi Monitor
Polarimeter Chicane
(Triple function on rear side)
(Charged and neutral particle acceptance)
Roman Pots
JLEIC Example
ZDC
JLEIC
Spectrometer Dipole

## Slide 14: eRHIC IR Design Aperture Schematic
B0
Q1
Q2
B1
C1X
B2A
B2B
Q0
Q1
Q1A
Q1B
Q2
Q1
Q2
B2
Lumi Monitor
e-Tagger
ZDC
Roman Pots
Forward Side
Rear Side
Protons
Electrons
±4.5 m Detector Space
eRHIC Example

## Slide 15: Detector Requirements
Exclusive Reactions in ep/eA:
Exclusivity criteria:
  eA: large rapidity coverage  rapidity gap events
    HCal for 1<h<4.5
  ep: reconstruction of all particles in event
    wide coverage in t (=pt2)  Roman pots
eA: large acceptance for neutrons from nucleus break-up
  Zero Degree Calorimeter
    veto nucleus breakup
    determine impact parameter of collision
 Poses stringent requirements on IR design
t=pt2
-4.5<h<4.5
scattered protons
break-up neutrons
Cuts: Q2>1 GeV, 0.01<y<0.85
DVCS – photon kinematics:

## Slide 16: Forward Scattered Neutrons
Diffractive physics in eA
Measure spatial gluon distribution in nuclei
Reaction:
 Momentum transfer t = |pAu-pAu′|2
suppress
by detecting
break-up
neutrons
Physics requires forward
scattered nucleus needs to
stay intact
Veto breakup through
neutron detection
Requirement:
Need at +/- 4 mrad beam element free
cone before the zero degree calorimeter
to detect the breakup neutrons
No nuclear dependence for heavy A
there neutrons are also critical to
reconstruct collisions geometry
L. Zheng, ECA, J-H. Lee arXiv:1407.8055
  precision neutron energy
  reconstruction  transv. size of ZDC
Au
Notes: spin-dependent gluon distribution

## Slide 17: eRHIC Forward Magnet Apertures
B0PF
Q1PF
C1XPF
Q2PF
B1PF
B2APF
B2BPF
Q0EF
Q1EF
ZDC
Forward Side
eRHIC Example
Spectrometer Dipole
Roman Pot Region
Closest Large Aperture, High Field Quadrupole

## Slide 18: Compact Forward Magnet Example
Direct Wind, NbTi, Actively Shielded eRHIC Q1PF
X (mm)
BY (T)
Main Coil
Shield Coil
Zero Field Region
Q1PF By Field
Rapt = 55 mm
Efficiency Factor = 90%
Gnet @ 275 GeV = 80.8 T/m
Budget for outer structure was set to accommodate the electron beam pipe.
Forward magnets must have large apertures to accommodate neutrons and forward charged particles.
But combination of large aperture and large gradient mean a large B-field at the coil....
However, the electron beam must be shielded from any large external fields.
“Pole Tip Field” = 4.4 T
Quad Field
Return Flux

## Slide 19: Very forward scattered particles
The very forward scattered particles are critical to detect for elastic/diffractive physics and not detectable in main detector.
Proton
Note:
Main detector acceptance starts at 35 mrad
Full pT coverage of proton critical for physics
pT = p’L sin(Q) p’L > 97% of pBeam
0.65 < Q (mrad) < 10
   0.2 GeV < pt < 1.3 GeV
small pT-acceptance limited by
beam divergence, emittance and beta-function
  rule of thumb keep 10s between
  Roman Pot and beam
large pT-acceptance limited by magnet apertures
eRHIC
JLEIC

## Slide 20: Shielding e-Beam Inside Spectrometer Dipole
B0 Magnetic Yoke
Superconducting Coils
e-Beam
Magnet is aligned with the e-beam, so p-beam enters at 25 mrad angle.
Experimental
Detector Here
1.3 T Cancel Coil Detail
Q0EF
eRHIC B0PF/Q0EF
Both eRHIC and JLEIC need to pass an e-beam through main aperture of first hadron spectrometer dipole (B0PF).
eRHIC even places a quad (Q0EF) inside.
This slide shows how, with a combination of a bucking dipole and passive shielding, this can be accomplished.
There are also other options for doing this with various tradeoffs possible.

## Slide 21: JLEIC Magnets and Component Integration
~2.6 m
ion beam
e beam
eQUS1
eQUS2
iBDS1
Detector Solenoid
JLEIC iQUS1a
(Magnet yoke not shown)
IR designs require production of many new challenging magnets (fortunately NbTi seems to be ok and Nb3Sn may not be needed).
JLEIC Example
But there are still quite significant engineering challenges in order to fit everything in very
restricted available
space!

## Slide 22: eRHIC Rear Side Magnet Apertures
Rear Side
Lumi Monitor
e-Tagger
eRHIC Example
Protons
Electrons
Tapered aperture magnets
Dipole bend to separate e-beam from lumi photons and quad synrad fan and analyze rear going electrons from physics events.
Synrad
Bethe-Heitler s
For eRHIC, the e-polarimetry chicane is located elsewhere.

## Slide 23: Requirements for Lepton Beam
Luminosity Detector
Concept:
Use Bremsstrahlung ep  epg as reference cross section
different methods:
  Bethe Heitler, QED Compton, Pair Production
Hera: reached 1-2% systematic uncertainty
Goals for Luminosity Measurement:
Integrated luminosity with precision δL/L< 1%
Measurement of relative luminosity:
physics-asymmetry/10  ~10-4 – 10-5
EIC challenges:
with 1033 cm-2s-1 one gets on average 23 bremsstrahlungs
photons/bunch for proton beam
 A-beam Z2-dependence
Need more sophisticated solution
BH photon cone < 0.03 mrad
 acceptance completely dominated by lepton beam size
zero degree photon calorimeter
high rate
Fast feedback for machine tuning
measured energy proportional to # photons
subject to synchrotron radiation
pair spectrometer
low rate
High precision measurement for physics analysis
The calorimeters are outside of the primary synchrotron radiation fan
Workgroup explores common issues
Lumi Monitor Schematic

## Slide 24: Managing Synrad Backgrounds at an EIC
B-Factories put our challenges in perspective.
Look to have only soft bends, well upstream of the IR region.
And use upstream masks to control upstream synrad that is unavoidably generated.
Look to limit the maximum synrad critical energy to be less than 40 keV (k-edge of W).
Look to let residual synrad fan pass completely though central detector region on to absorbers and masks far from IP.
Look to block as much synrad backscatter albedo as possible with downstream masks.
For eRHIC rear side design the rear side apertures are tapered to allow passage of synrad cone generated by upstream quads.
In addition to using existing synrad codes to estimate and mitigate the anticipated backgrounds, we also collaborate with B-factory experts who have a lot of experience dealing with such backgrounds.
B-Factory designs must take into account complex synrad masking

## Slide 25: Detector Beam Pipes for an EIC
JLEIC Central Beam Pipe
eRHIC Central Beam Pipe
Small diameter, thin walled Be in center region.
Smooth tapers and transitions to limit energy deposited by beam in trapped modes (wakes).
Need to provide beam tube cooling and for any Higher Order Mode (HOM) damping absorbers.
Need to provide adequate vacuum pumping.
eRHIC / Beast plans include in situ bakeout.

## Slide 26: ... and there is still plenty more work that needs be done to realize an EIC
EICUG IR / Luminosity Working Group
interface between accelerator / IR design and the
physics requirements
proper implementation of the physics program in particular for forward / backward detection
Conveners:
• Accelerator / IR: C. Montag (BNL), V. Morozov (JLab)
• Physics: C. Hyde (ODU), A, Kiselev (BNL)
EICUG Working Group on Polarimetry
plan / develop the optimal methods and techniques for
measuring the electron and ion beam polarization with high
precision
Conveners
E.-C. Aschenauer (BNL), D. Gaskell (JLab)

## Slide 27: ...and I would like to thank many people
Elke-Caroline Aschenauer
Roman Martin
Tim Michalski
Vasiliy Morozov
Robert Palmer
Renuka Rajput-Ghoshal
Dmitry Romanov
Michael Sullivan
Mark Wiseman
Holger Witte
...for much of the material presented today.