|  | Task Hazard Analysis (THA) Worksheet (See ES&H Manual Chapter 3210 Appendix T1 Work Planning, Control, and Authorization Procedure) |  |
| --- | --- | --- |

| Author: | Michael Drury | Date: | 8/14/18 | Task #: If applicable |  |
| --- | --- | --- | --- | --- | --- |
| Complete all information. Use as many sheets as necessary |
| Task Title: | LCLS II Cryomodule Testing in the LERF | Task Location: | LERF |
| Division: | Accelerator | Department: | SRFOPS | Frequency of use: | Variable |
| Lead Worker: | Michael Drury |
| Mitigation already in place: Standard Protecting Measures Work Control Documents | Credited Passive Engineered Controls (See Table 5-1 Final Safety Assessment Document Rev 7a): Permanent Shielding including Labyrinths (Prompt Ionizing Radiation) Movable and Relocatable Shielding (Prompt Ionizing Radiation) Nitrogen Supply Orifices (ODH) Credited Active Engineered Controls (See Table 5-1 Final Safety Assessment Document Rev 7a): PSS System Level Controls (Prompt Ionizing Radiation) Critical Devices Access Controls Sweep Procedures Interlocks Multiple Safety Functions Alarm and Warning Devices ODH Monitoring and Alerts Credit Controls reduce risk levels for addressed hazards to no higher than RC 2. SRF-16-62027-OSP Cryomodule Installation SRF-16-61608-OSP Cryomodule Removal SRF-16-63829-OSP RT valve cabling activities |

| Sequence of Task Steps | Task Steps/Potential Hazards | Consequence Level | Probability Level | Risk Code (before mitigation) | Proposed Mitigation (Required for Risk Code >2) | Safety Procedures/ Practices/Controls/Training | Risk Code (after mitigation |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Cryomodule Installation and Preparation for Testing: Electric Shock Ion pump power supply Cold cathode gauge high voltage +/- 3kV at 5 mA | H | M | 4 | Only SHV connectors are used. This type of connector makes the ground connection first when plugging in and breaks it last when unplugging the connector | All voltage sources are “plug in “. Must unplug before servicing. Power-down procedures are in place. | 1 |
|  | Cold cryomodule ODH hazard Pressure relief due to cryogenic failure | L | M | 2 | Credited Active Controls: ODH Monitoring and Alert System. Defense in Depth: LERF Door Configuration slows He gas entry into stairwells. Cryomodule Primary Reliefs vent to above-ground | ODH assessment and rating of LERF Vault. ODH2 training and Escape Pack training required for all LERF Testing personnel. Personal escape packs and oxygen monitors required for ODH2 areas. | 1 |
|  | Cold cryomodule ODH hazard: Potential for blocked egress due to equipment staged around cryomodules impedes evacuation during an ODH event. | H | L | 3 |  | ODH Training Staff advised via this OSP to maintain egress path around the cryomodule. | 1 |
|  | Cold cryomodule ODH hazard: Outlet valves closed during routine operation | L | L | 1 | Credited Active Controls: ODH Monitoring and Alert System. Defense in Depth: LERF Door Configuration slows He gas entry into stairwells. Cryomodule Primary Reliefs vent to above-ground | Primary Circuit Outlet valves are normally locked in Open position. For situations in which valves are not locked open See SRF-16-63829-OSP OSP for Connecting and Disconnecting the RT Valve During Commissioning ODH assessment and rating of LERF Vault. ODH2 training and Escape Pack training required for all LERF Testing personnel. Personal escape packs and oxygen monitors required for ODH2 areas. | 1 |
|  | ODH Hazard: Leak of warm nitrogen service line inside tunnel or LERF vault | M | M | 3 | Credited Controls: Nitrogen lines outfitted with flow restricting orifice PSS: ODH Alarm (sensors positioned for N2 and He) Defense in Depth: Nitrogen supply line solenoid valves | ODH Training | 1 |
|  | Energizing 1300 MHz SSA’s 480 V Hazards Arc Flash from Disconnect | H | M | 4 | Safety glasses Hearing protection Heavy duty leather glove Long sleeve shirt and long pants both of a non-melting/non-flammable material | General Electrical Training SAF603A Electrical Safety Awareness SAF603N Basic NFPA-70E Training SAF104 LOTO | 1 |
|  | Non- Ionizing Radiation due to RF leakage from waveguide: RF burns, eye damage, tissue heating due to improperly assembled waveguide joints or component failure or open waveguide | M | L | 2 | Active Control (Defense in Depth): Waveguide pressurized and interlocked through PSS prevents exposure to personnel outside enclosure. RF disabled if interlock not met. Personnel Safety System Access Controls and Interlocks insure that 480 VAC not applied to Solid State Amplifiers when LERF vault occupied. | PSS Sweep procedures. Minimum Staffing Levels during Testing. SAF104 LOTO | 1 |
|  | Prompt Ionizing Radiation Inherent hazard from operating high gradient cavities in vacuum. | M | M | 3 | Permanent Shielding in place (concrete enclosure) Personnel entry to enclosure through labyrinth. Movable Shielding Blocks at LERF Truck Ramp. Position Interlocked Personnel Safety System Access Controls and Interlocks insure that 480 VAC not applied to Solid State Amplifiers when LERF vault occupied. CARM monitoring and warning devices | PSS Sweep procedures. Minimum Staffing Levels during Testing. Signage Training: All testing personnel must have Rad Worker 1 training. All testing personnel must read and sign any applicable RWP’s. | 1 |
|  | Cryo distribution system to LCLS II CM / vacuum / pressure, cryogens Operation of the LCLS II CM: vacuum / pressure, cryogens | M | M | 3 | Pressure / vacuum design by competent Design Authorities for cryo distribution and CM | Reference design information here… | 1 |

| Highest Risk Code before Mitigation: | 4 | Highest Risk Code after Mitigation: | 1 |
| --- | --- | --- | --- |

When completed, if the analysis indicates that the Risk Code before mitigation for any steps is “medium” or higher (RC≥3), then a formal Work Control Document (WCD) is developed for the task.  Attach this completed Task Hazard Analysis Worksheet.  Have the package reviewed and approved prior to beginning work.  (See ES&H Manual Chapter 3310 Operational Safety Procedure Program.)

Form Revision Summary Periodic Review – 08/13/15 – No changes per TPOC Revision 0.1 – 06/19/12 - Triennial Review. Update to format. Revision 0.0 – 10/05/09 – Written to document current laboratory operational procedure. ISSUING AUTHORITY TECHNICAL POINT-OF-CONTACT APPROVAL DATE REVIEW DATE REV. ESH&Q Division Harry Fanning 08/13/15 08/13/18 0.1 This document is controlled as an on line file. It may be printed but the print copy is not a controlled document. It is the user’s responsibility to ensure that the document is the same revision as the current on line file. This copy was printed on 11/7/2018.

# Text boxes

Click

For Word Doc