## Slide 1: SC1R Insulation Strategy
Nate Laverdure

## Slide 2: Overview
Purpose for discussion
Insulation on:
  Internal piping spools
  LN2 shield
  CC casings
  Top torispherical head of vacuum vessel
  Cylindrical shell of vacuum vessel
  Internal frame

## Slide 3: Insulation – Internal piping spools
Preferred method
Spirally-wound cylinder of 30 layers
Cylinder length is equal to roll length (~50”) of the source material
Butt joints between adjacent sections:
    Edges trimmed, spaced ~1/2” apart, and taped together at the accessible outer layer

## Slide 4: Insulation – Internal piping spools
When the preferred method is not practical
Wrapped blanket of 30 layers
Longitudinal seam of wrapped blanket:
    Interleaved in groups of 5-10 layers with at least 2” overlap
    Folded-over “praying hands” technique
  Butt joints between adjacent sections:
    Interleaved in groups of 5-10 layers with at least 2” overlap
    Edges trimmed, spaced ~1/2” apart, and taped together at the accessible outer layer

## Slide 5: Insulation – LN2 shield
Treated as if it were (very large OD) piping
Wrapped blanket of 30 layers
Longitudinal seam of wrapped blanket:
    Interleaved in groups of 5-10 layers with at least 2” overlap
    Folded-over “praying hands” technique
  Butt joints between adjacent sections:
    Interleaved in groups of 5-10 layers with at least 2” overlap
    Edges trimmed, spaced ~1/2” apart, and taped together at the accessible outer layer

## Slide 6: Insulation – CC casings
Reference document

## Slide 7: Insulation – CC casings
Reference document

## Slide 8: Insulation – CC casings
Design document [71220-1263]

## Slide 9: Insulation – Top torispherical head of vacuum vessel
Blanket of 20 layers total
  4 interleaved panels of 5 layers each
Internal structural features
  Tagged with nylon garment label tags
  Seams sewn with Nomex lacing cord

## Slide 10: Insulation – Top torispherical head of vacuum vessel
Final shape is templated from interior of head

## Slide 11: Insulation – Top torispherical head of vacuum vessel
External attachment
  Suspended by hook & loop (velcro), sewn to blanket with lacing tape
  Held against top head by skeletal frame

## Slide 12: Insulation – Top torispherical head of vacuum vessel
Held against top head by skeletal frame

## Slide 13: Insulation – Top torispherical head of vacuum vessel
Held against top head by skeletal frame

## Slide 14: Insulation – Top torispherical head of vacuum vessel
Held against top head by skeletal frame

## Slide 15: Insulation – Cylindrical shell of vacuum vessel
Blanket of 20 layers total
  4 butting panels of 5 layers each
Shape
  Bottoms of panels drape onto lower head and continue under internal platform
Internal structural features
  Tagged with nylon clothes label tags
External attachment
  Blanket panels are suspended from row of studs inside the top head
  Holes have sufficient pull-out strength for the blanket weight

## Slide 16: Insulation – Cylindrical shell of vacuum vessel
Panels arranged in 4 rows of 8
Simple (not interleaved) butt joint between sides of adjacent panels
  Edges spaced ~1/2” apart and taped together at the accessible inner layer
Successive rows of panels are staggered, covering these butt joints

## Slide 17: Insulation – Internal frame
Similar to top head blanket
  Blanket of 20 layers
  Templated from as-built platform
  Internal butt joints within blanket are interleaved
  Blanket overhangs 6” over all sides, overhangs are taped to frame

## Slide 18: SC1R Insulation Strategy
Nate Laverdure