## Slide 1: Cavity/CM Considerations for CW Operation
Cryogenic loads and cryogen distribution
End Group cooling: HOM antenna redesign
HOM loads and suppression requirement
Coupler design and cooling
Cost, gradient, Qo, QL and RF power
Achieving higher cavity Qo
Microphonics - size and suppression
Chris Adolphsen, SLAC, Sept 12, 2013 Visit to JLAB

## Slide 2: 8 Cavity CM Heat Loads (16 MV/m, Qo = 3e10)
(12 W for ILC)
With high dynamic load, may be able to lower cost or improve
performance with somewhat higher static load

## Slide 3: 8 Cavity CM Heat Loads (16 MV/m, Qo = 3e10)
(16 W for ILC)

## Slide 4: 8 Cavity CM Heat Loads (16 MV/m, Qo = 3e10)
Total: The AC cryoplant power required per CM is 106 kW assuming a 30% overhead – with 32 CMs, a 3.4 MW plant is required.
(155 W for ILC)

## Slide 5: Modifications to 2 K Pipes to Accommodate Larger Heat Flow
Slightly larger nozzle from helium vessel to 2-phase pipe
  Increase from 55 mm to about 70 mm
Slightly larger 2-phase pipe
  Depends on string lengths and liquid management plan
  Retain option for 1.8 K in all piping
  Increase from 72 mm to about 90 mm
Segmentation of 2 K liquid and 2 K flow distances may also impact this pipe sizing
The cryomodule itself will be the most likely source of fast (< 1 sec) pressure changes, so attention to piping and valve configurations are critical

## Slide 6: Separate liquid management in each cryomodule but no external transfer line
650 MHz Cryomodule Design, 21 Feb 2011
Page 6

## Slide 7: JLAB C100 ‘Stand-Alone’ Cryomodule

## Slide 8
J. Sekutowicz
HOM Antenna Heating

## Slide 9
J. Sekutowicz

## Slide 10: Antenna Modifications for E-XFEL
J. Sekutowicz
“The feedthroughs are made of high conductivity materials, pure niobium, molybdenum and sapphire. They will be connected thermally to the 2-phase tube with copper braids for better heat transfer to the 2 K environment.”

## Slide 11: Beam Line Absorbers (One per CM)
J. Sekutowicz
“Total deposited HOM power by the nominal XFEL beam will be 3.81 W per cryomodule, if no synchronous excitation will take place. Most of this power, ~ 85%, will be dissipated in the beam line absorbers (BLA).... In the absorber design we took into account operations in the cw/lp modes, in which beam deposited power can be as high as 100 W.”

## Slide 13: Reduced Dipole HOM Damping
With 1/30 of the current, 1/3 lattice beta, 1/30 of the linac length and 10 times the emittance of the ILC, can we increase QL considerably to simplify the damping ?
Also, would randomly varying the bunch timing (modulo a 1.3 GHz period) about the nominal 1 us bunch spacing significantly reduce the damping requirement

## Slide 14: Cornell 200 mA, 7 Cell Cavity No HOM Ports but Larger Beam Pipe and One Beamline Absorber/Cavity
200 W HOM Power/Cavity
Need such damping if eventually
convert LCLS IISC to an ERL

## Slide 15
Coaxial Power Coupler
Input
Power
Powering the Cavities
Power coupler design complicated by need for tunablity (Qext), dual vacuum windows and bellows for thermal expansion.
For ILC, TTF3 design processed to 1.1 MW with 1.6 ms pulses – would run at only 5-6 kW for LCLS IISC, so may not need extensive rf processing, but would need to improve the warm section cooling (4 kW average for 10 Hz TESLA ).

## Slide 16: Inner Conductor Temperature Distribution with Different Thicknesses of Copper Coating for 15 kW CW RF Power
10µm on outer conductor with RRR=10
Shilun Pei

## Slide 17: JLAB Upgrade 7-Cell Cavity with WG Couplers
l/4 waveguide RF input coupler
Fundamental Power Coupler (FPC)
Cu-plated waveguide between RT and 2 K
Warm ceramic RF window
SST helium vessel
HOM coupler (2)
RF reference probe
Warm tuner actuator not shown

## Slide 18
They assumed Q0=2x1010 - with higher Qo, cost optimal gradient increases – for now assume 16 MV/m and Qo = 3e10 for LCLS IISC, which pushes the cooling limit of a single cryoplant for a 4 GeV linac.
RF power
Cryoplant
Cryomodules & enclosure
Total cost, construction + 15 yrs operations
Total cost, construction only
Cryomodules & enclosure
Cryoplant
RF power
Relative NGLS Cost versus Cavity Gradient
From John Corlett’s June 2013 Cornell TTC Talk

## Slide 21
Cornell Horizontal Test 3
Full cryomodule assembly with power coupler and beam absorbers (cavity prep included a HF rinse)
Qo >= 3e10 at 16 MV/m in a CM is possible at 1.8 K

## Slide 22
New Surface Treatments Developed at FNAL for Higher Q
Treatment | Q @ 16 MV/m, @ 2K, 1.3 GHz Demonstrated on several cavities | Improvement over baseline, component improved | Maximum Q achievable with ideal cool down (16MV/m, 2K, 1.3GHz)
EP+120C (standard ILC) | 1.5-1.7e10 | -- | ~2.2e10
EP + 120C + HF rinse | ~2.3e10 | ~30-40% , residual | 3e10
EP + Annealing + no chemistry | ~2.7e10 | ~50-60%, residual | 3e10
EP + Gas (nitrogen or argon) bake + EP | ~4e10 | ~100-150%, BCS and residual | 6.75e10
Golden opportunities!

## Slide 23
Parameter | Value | Comment
Gradient | 16 MV/m | On crest
Beam Current | 0.3 mA | 
Cavity QL | 4.12 e7 | Based on formula on next slide – minimizes power for 10 Hz microphonics (MP) offset
Max Power per Cavity ( w MP w/o overhead) | 5.72 kW | Power with 10 Hz MP offset – no overhead
Max Power per Cavity (w MP w overhead) | 6.32 kW | Assume 94% transmission and 4% overhead
Max Power for 48 cavities (w MP and w overhead) | 303 kW | Either one source per cavity so can track MP locally or one source for 48 cavities
RMS MP offset allowed with a 300 kW source | 9 Hz | For Gaussian distributed MP
RF Power, QL and Overhead

## Slide 25: Relative Power vs QL (Units of 1e7) with a 10 Hz Offset

## Slide 26: CM Gradient (Vector Sum) Stabilization at DESY
RF-feedback off
Standard deviations for:
Amplitude = 1.5E-3
Phase = 0.5°
Goal: Stability of the vector sum for the cw operation with the new µTCA LLRF.
Conditions: Eacc = 3.5 MV/m, mode cw, piezo feedback off, bias on.
Test Result:
Conclusion:
New µTCA RF-feedback improves amplitude and phase stability by factor of 24 and 51 respectively, and fulfills spec for the XFEL linac.
RF-feedback on
Standard deviations for:
Amplitude = 6.2 E-5
Phase = 0.0098°
1s
1s
Vector sum
Vector sum
phase
phase
QL = 1.5e7

## Slide 27: JLAB Upgrade Cavity Microphonics
Microphonic Detuning* | C100-1 | C100-4
RMS (Hz) | 2.985 | 1.524
6s(Hz) | 17.91 | 9.14
Determines the Feedback Gain needed for control.
Effects are driven by QL and the available klystron power for lightly loaded cavities
Cavity C100-1-5
Cavity C100-4-5
Minor change to the tuner pivot plate substantially improved the microphonics for the CEBAF C100 Cryomodules.
While both meet the overall system requirements the improved design has a larger RF power margin

## Slide 28: Microphonics compensation at HZB
Reduced detuning by an order of magnitude
Achieved „open loop“ phase stability:13.2°  2.0°
0.02° phase stability achievable
Compensate multiple resonances
Needs implementation into LLRF control and operation with beam
SFFT
w/o
control
sf = 2.52 Hz
feedback
sf = 0.89 Hz
feedback &
feed-forward
compensation
sf = 0.36 Hz
Time (s)
Frequency (Hz)
Detuning (Hz)
Detuning (Hz)
# events
Detuning (Hz)

## Slide 29: ‘BESSY’ Microphonics Example
Resulting Energy Variation over Time: 9e-4 variation in a cavity energy gain, which if uncorrelated cavity to cavity, would produce 7e-5 beam energy variation at the end of the linac (ignoring the BCs and the various FB systems)
41 Hz mode driven randomly to yield a 1.5 Hz rms frequency variation – then solve cavity field level with a constant rf input and beam current
Claudio Rivetta

## Slide 30: Summary
Recent improvements in cavity cooling, gradient, Qo and microphonics bode well for future CW SCRF linac driven light sources.
Let’s work together to bring this together and build a next-generation CW linac.