## Slide 1: Requirements for Efficient CW SRF Cryomodules
Andrew Burrill
An efficient cryomodule should achieving optimum performance
with minimum wasted effort or expense.

## Slide 2: What is a CW SRF Cryomodule?
A collection of precisions engineered and fabricated components (SRF Cavities – Focusing Elements – Couplers – HOM Absorbers – Tuners – Magnetic and Thermal Shields etc.) designed to operate continuously in or near a cryogenic environment. - The foundation of the accelerator.
What does it needs to do? Operate all the time in the most stable and cost effective manner possible.
What it is not: These are not pulsed machine cryomodule
Dynamic Load >> Static Load
Thermal management becomes even more critical
Power handling capabilities of auxiliary components is much greater
Operating costs are much higher

## Slide 3: The CW difference
Proceedings of IPAC’10, Kyoto, Japan

## Slide 4: CW SRF Cryomodule I
Electron Accelerator
Linac module
  Multiple 5-9 cell cavities
Injector module
  Single cavity
  May incorporate booster cavity
Booster module
  Multiple one or two cell cavities
JLab C100
KEK Booster
BERLinPro

## Slide 5: CW SRF Cryomodule II
Ion Accelerator
Low β structures
  λ/4 or λ/2 resonator & magnets
  Spoke resonator & magnets
Medium β elliptical cavity module
High β elliptical cavity module
ATLAS λ/4 CM
Project X SSR CM
Project X β=0.9 CM

## Slide 6: What are you trying to build?
R&D, Proof of Principle, Accelerator
Demonstrate something new
Often built with limited resources
Time to explore cryomodule options
  Cavity design
  Tuner
  HOM filters / absorbers
  Couplers
  Thermal management
Some uncertainty about cryomodule performance
Planned operation is usually less than 24/7/365
Number of modules being built is usually small, often 1
Outside vendors are often building first articles for use in the CM
Limited/No Spares
Cryogenic system is often “turn-key”, not necessarily optimized for the accelerator
  Lower efficiency, more $$ to operate
Large Scale User Facility
24/7/365 operation
Longer development time
  Prototypes already built and tested
Far less uncertainty
Not the time to be de-bugging the system
Much more detailed budget and labor estimates
Workforce focused on cryomodule production
Suppliers have been vetted
Spares have been ordered
Cryogenic system has often been optimized for the accelerator
  Higher efficiency, more cost effective
Notes: Things that weigh on the decisions you make for the CM

## Slide 7: Universal High Level Requirements
Highly reliable.
  Accelerator downtime should not be due to the CM itself
SRF Cavities need to operate efficiently
Large power dissipation in the cavity/CM
Overall cost of the cryomodule design, construction and operation needs to be As Low As Reasonably Allowable
Full project cost analysis needs to be done to minimize the overall cost
Where’s the BEAM!

## Slide 8: Requirements I
Highly reliable. Accelerator downtime should not be due to the CM itself
  Cavities should operate in a stable regime
    No planned operation within 20% of the multi-pacting regime
    Operate below strong field emission regime (flat part of Q vs E curve)
  HOM absorbers thermal management needs to be understood
    Difference between vertical testing and cryomodule performance must be understood
  High power couplers and windows should be robust
  Heat intercepts sized and demonstrated
  High current leads for magnets should be properly thermally managed
  Insulating vacuum system should be robust and designed with proper pressure relief valves to avoid damage to cavities
SRF Cavities need to operate efficiently
Large power dissipation in the cavity/CM
Overall cost of the cryomodule design, construction and operation needs to be As Low As Reasonably Allowable
Full project cost analysis needs to be done to minimize the overall cost

## Slide 9: Requirements II
Highly reliable. Accelerator downtime should not be due to the CM itself
SRF Cavities need to operate efficiently
  RF power usage
    Well understood coupler design and cavity/coupler/CM interface
  Cryogenic consumption
    Both static and dynamic losses
    Proper heat intercepts
    Calculations of cost/Watt to intercept with LN2, 80K He, 5K He
  HOM management
  Minimize vibrations that reach the cavity
    Control the microphonics
  Provide precise cavity alignment in each module and between modules
  Excellent magnetic shielding design
    Attempt to provide the same reduction of magnetic field in the CM as in the vertical testing dewar
    Elimination of magnetized components or materials inside the cryomodule
  Robust vacuum system, redundant RF window design
Large power dissipation in the cavity/CM
Overall cost of the cryomodule design, construction and operation needs to be As Low As Reasonably Allowable
Full project cost analysis needs to be done to minimize the overall cost

## Slide 10: Requirements III
Highly reliable. Accelerator downtime should not be due to the CM itself
SRF Cavities need to operate efficiently
Large power dissipation in the cavity/CM.
  Optimum operating temperature needs to be well understood
  2K cryogenic system needs to be properly designed to handle the large power dissipation, (>30 watts/ cavity in a 7 cell Linac module)
    HV chimney sized to handle >30 watts/cavity
    Potential pressure drop in 2 phase pipe needs to be understood
    Gas flow rate in the 2 phase pipe needs to be controlled
    Pressure stability needs to be excellent, less than 0.1% pressure fluctuation
      16 μbar for 1.8K operation
      38 μbar for 2.07K operation
    Great care must be taken if a pulsed cavity/cryomodule design is adopted
  Cryogenic plant needs to be matched to the operating condition to reduce overall cost.
  Large scale accelerators benefit from a custom engineered cryogenic system
    http://www.jlab.org/conferences/cryo/
Overall cost of the cryomodule design, construction and operation needs to be As Low As Reasonably Allowable
Full project cost analysis needs to be done to minimize the overall cost

## Slide 11: Requirements IV
Highly reliable. Accelerator downtime should not be due to the CM itself
SRF Cavities need to operate efficiently
Large power dissipation in the cavity/CM.
Overall cost of the cryomodule design, construction and operation needs to be As Low As Reasonably Allowable
  Re-use existing designs where possible
    Cavities, tuners, couplers
    Learn what has worked for your colleagues, and especially what hasn’t.
    Take advantage of existing infrastructure, tooling and drawings to reduce the cost and timeline of the project.
    A prototype CM needs to be built and tested after the design is frozen
  Optimize operating conditions taking into account CM cost, Cryogenics and RF wall plug efficiency
Full project cost analysis needs to be done to minimize the overall cost

## Slide 12: Closing Thoughts
Utilize what is available in the community
Improve on existing designs
Pressure vessel code compliance
Participate in fruitful collaborations
Communicate the successes and the failures to help others avoid the same pitfalls.
Thank you